## Slide 1: Lecture1-2 Introduction (I)
Computer Organization and Architecture

## Slide 2: Today’s Topic
Why Computer Organization & Architecture are important
Logistics & Disciplines
Brief History of Computer Architecture
Classification of Computers
What is Computer Organization & Architecture
0.0

## Slide 3: NSCSCC 2017
Fastest CPU in NSCSCC 2017
  MIPS
  92.6MHz in Xilinx Arty FPGA (with 40% IO delay Assumption)
  3.712x Loongson Open Source CPU

## Slide 4: NSCSCC 2018
The fastest two CPUs in NSCSCC 2018
  MIPS
  135MHz/122MHz in Xilinx Arty FPGA
  74.146x/70.679 Loongson Open Source CPU
“西工大队通过在关键路径上一点点细抠进行系统性能调优，特色明显。体现出他们对技术的精益求精的追求，对自己能力极致的挖掘，这是需要所有参赛选手应该追求的品质，是系统能力培养方面的重要方向”。
-----------刘卫东（清华大学教授，代表组委会的点评）

## Slide 5: NSCSCC 2019
The first 4-way superscalar CPU in the competition
  Out of Order Execution，Register Renaming、Branch Prediction，Write Buffer，。。。。。。
Notes: 我们神奇的地方就在于此，我们的主频只有清华的不到一半，但是性能几乎一样，这种技术优势，只有内行才能看出来；我们引领整个比赛的技术发展方向，每次我们参赛的技术，当年的比赛未必受到所有人的认可，但是在第二年都会成为大赛的主流技术。

## Slide 6: NSCSCC 2021
The fastest 3 CPUs in the Competition
Run at 155MHz, 150 MHz, and 145 MHz respectively.
Cache, MMU. Running Linux.
组委会的点评：“……对于这样复杂度的设计，150多MHz的主频已接近于组委会提供的硬件平台的极限。”

## Slide 7: NSCSCC 2022
The fastest 3 CPUs in the Competition
Run at 155MHz, 150 MHz, and 145 MHz respectively.
9 Students achieved the individual award.
组委会点评：…近年来，各支参赛队形成了自己的风格，比如西工大代表队一直在电路优化方面努力，工作主频不断提高，就如“天下武功，唯快不破”…

## Slide 8: Why Computer Organization & Arch
1.0
Image credits: uber, extremetech, anandtech

## Slide 9: Why Computer Organization & Arch
Embarrassing if you are a BS in CS/CE and can’t make sense of the following terms: DRAM, pipelining,cache hierarchies, I/O, virtual memory, …
Embarrassing if you are a BS in CS/CE and can’t decide which processor to buy: 3.0 GHz 2-core KabyLake or 3.6 GHz 8-core Zen (helps us reason about performance/power), …
Obvious first step for chip designers, compiler/OS writers
Will knowledge of the hardware help you write better programs?
1.0

## Slide 10
1.1
Programmers‘ Essential About Hardware?
Must know how to evaluate program performance and energy
Memory management: if we understand how/where data is placed, we can help ensure that relevant data is nearby
Thread management: if we understand how threads interact, we can write smarter multi-threaded programs
 Why do we care about multi-threaded programs?

## Slide 11: Example
200x speedup for matrix vector multiplication
Data level parallelism(DLP, SIMD): 3.8x (Ch. 3)
Loop unrolling and out-of-order execution， Instruction Level Parallelism(ILP):2.3x (Ch.4)
Cache blocking, Memory Hierarchy Optimization: 2.5x (Ch. 5)
Thread Level Parallelism, parallel for loops in Multicore systems: 14x (Ch. 6)
Further, can use accelerators to get an additional 100x.
1.1

## Slide 12: Logistics & Disciplines
Instructor: Jianfeng An, Meng Zhang and Danghui Wang anjf, zhangm, wangdh@nwpu.edu.cn Room 440/411/436 CS Building
Books:
  Textbooks: “Computer Organization and Design” ,the 6th Edition, Patterson and Hennessy, 2013
  Chinese Version, Translated by Danghui Wang, Jichang Kang and Jianfeng An, 2022
  Reference: “Computer Architecture: A Quantitative Approach”, the 5th Edition, Hennessy and Patterson,2011
  Computer Organization, Shuofei Tang
Slides: English
Grading Information
  Homework and attendance: 30%
  Final Exam:70%
  Extra bonus:?
2.0

## Slide 13: Brief History of IT (Information Tech)
3.0
Invention of writing, Sumer,
3500 B.C.
Oracle Characters, China, ~3000 years ago
Papermaking, Lun Cai,
China, 2nd Century
Typography, Sheng Bi, China,
Mid 11th Century
Modern movable type printing, Johannes
Gutenberg, Germany,
Mid 15th Century

## Slide 14: Brief History of IT (Information Tech)
Abacus，~500 B.C.，China
3.0

## Slide 15: Brief History of IT (Information Tech)
Difference Engine，Charles Babbage，1832
3

## Slide 16: Brief History of IT –Difference Engine
A machine to compute mathematical tables
Any continuous function can be approximated by a polynomial
Any polynomial can be computed from difference tables
Mechanical Registers
Steam engine drived output
3-order polynomial ，15 decimal digital
3.0

## Slide 17: Brief History of IT – Analytical Engine
1834，Babbage
3.0

## Slide 18: Brief History of IT-The first programmer
Ada Byron，1815-1852
3.0

## Slide 19: Brief History of IT (Information Tech)
3.0
John Mauchly, J. Presper Eckert and Von Neumann ENIAC
Micro Processor leverages Computing
Everything is online

## Slide 20: Brief History of Chinese Compt. Tech.
107 General Purpose Digital Computer
1960.04
3.0
Professor Peisu Xia(9123.07.28-2014.08.27）

## Slide 21: Brief History of Chinese Compt. Tech.
3.0
Professor Jichang Kang(1930.03.14-2018.01.09）
114 Computer（SSS-1型数字式射击瞄准计算机）
1974.12
我国第一台机载火控计算机

## Slide 22: Brief History of Chinese Compt. Tech.
3.0
Galaxy-1
The First Supercomputer whose performance is 100 + MOPS
1983.12.22

## Slide 23: Brief History of Chinese Compt. Tech.
3.0
Tianhe-2（Milyway-2）
2013~2016：The fastest supercomputer in the world
国防科技大学

## Slide 24: Brief History of Chinese Compt. Tech.
3.0
Sunway TaihuLight
2017：The fastest supercomputer in the world
国家并行计算机工程技术研究中心

## Slide 25: Brief History of Chinese Compt. Tech.
Prof. Weiwu Hu
Loongson CPU
3.0

## Slide 26: Brief History of Chinese Compt. Tech
3.0
CPU Die
CPU Die
I/O Die
鲲鹏开放主板
鲲鹏服务器
分析扫描工具
代码迁移工具
鲲鹏是计算平台
制程工艺领先：业界领先7nm制程，
多Die合封的Chiplet架构
自研多核内核：自研CPU内核算力提升50%，自研片间互联，支持多路互联
率先支持下一代网络和接口：支持8通道内存控制器和100GE端口
处理器->单机->集群，鲲鹏开放硬件平台
完备的软件工具链，发挥鲲鹏最佳性能
性能优化工具
加速库
鲲鹏是SoC
鲲鹏---华为

## Slide 27: Brief History of Chinese Compt. Tech
华为“鲲鹏”处理器
3.0
32核，2.4 GHz主频
SPECint性能匹配业界中端，功耗低至75 W
支持4通道DDR4控制器
支持PCIe 3.0和SAS/SATA 3.0
集成板载GE/10 GE网络
支持2路互联
7nm制程，数据中心ARM处理器
计算核数提升1倍，最多64核
SPECint性能提升超过2倍
内存通道数提升1倍，支持8通道DDR4控制器
支持PCIe 4.0和CCIX
集成板载100 GE网络和加密、压缩等引擎
支持2路或4路互联
鲲鹏916
鲲鹏920
支持多路互联的ARM处理器

## Slide 28: Brief History of Chinese Compt. Tech
基于鲲鹏主板的多样化计算产品
3.0
鲲鹏主板开放
共享接口与设备规范
整机参考设计
共享工程能力
整机参考设计指南
(含机箱、散热、供电等设计)
部件与OS兼容性列表
主板(含鲲鹏处理器)
主板接口规范
BIOS软件 & 规范
BMC芯片/软件 & 设备管理规范
PC
服务器
打造多样化计算产品

## Slide 29: Brief History of Chinese Compt. Tech
3.0
17年的工程工艺积累
高速互联
可靠
设计
质量品控
40度以上异常高温运行
56G/112G板级高速互联
无源背板&三重硬盘抗震
故障率低于业界15%
液冷
散热
  5280
  4U40盘存储型
  X6000
  2U4节点高密型
  2280
  2U2路均衡型
数据中心
存储密集型
计算密集型
  1280
  1U2路高密型
  5290
  4U72盘存储型
  (新产品)
  (新产品)
  (新产品)
  2480
  2U4路高性能型

## Slide 30: Brief History of Chinese Compt. Tech.
Tsinghua University
Northwestern Polytechincal University
航空计算技术研究所
北京航天微电子技术研究所
……
3.0

## Slide 31: 2 Great Inventions of IT
ENIAC (Electronic Numerical Integrator and Computer, Feb 14, 1946)
  Beginning of computers as a main role in IT Roadmap
3.1
Glen Beck (background) and Betty Snyder(foreground) program ENIAC in BRL building 328. (U.S. Army photo)
Photo of (from left) J. Bardeen, W. Shockley and W. Brattain, the inventors of the transistor, 1948.
Jack Kilby's original integrated circuit (IC)
Transistor (1946) and IC (1957)
  Moore’s Law is the observation that the number of transistors in a dense integrated circuit doubles approximately every two years.
    Memory Size
    Processor Integrations
    Communication Bandwidth of Computer
Notes: Betty Snyder, one of the original programmer of ENIAC.
Actually, the first IC was designed by Jack Kilby in TI’s lab. However, as the business consideration, applying patent, the Lab leader kept it as a TI’s top secret, which also kept Jack Kilby’s Noble till 1970’s for his JK FlipFlop.

## Slide 32: Information Tech
3.1
Information Theory
Eg. Nyquist–Shannon sampling theorem
Computing Theory
Eg. Turing Machine
Von Neumann Structure
IT
(Information Technology)

## Slide 33: Dematerialization of Human Society
Human Civilization has been dematerialized via Cyberization Tech
  Terminology
    ops, bytes, bits/second(bps), pixels, and sensors/actuators
  Media began to be changed into electrons, magnetics and photons held in semiconductors from Atoms
  Cyberization Tech
    Bridge the gap between Atoms of material and electrons, photons even quantum
3.2

## Slide 34: The Computer Revolution
Progress in computer technology
  Underpinned by Moore’s Law
Makes novel applications feasible
  Computers in automobiles
  Cell phones
  Human genome project
  World Wide Web
  Search Engines
Computers are pervasive
3.3

## Slide 35: Information Data Storage
Data Type | Per Hour | Per Day (Per 4-year) | Whole life of person
Reading Lecture | 200K | 2-10M(G) | 60-300G
Speaking (120 wpm) | 43K | 0.5M(G) | 15G
Audio (1KBps) | 3.6M | 40M(G) | 1.2T
POTS Video (50Kbps) | 22M | .25G(T) | 7.5T
VHS (200Kbps) | 90M | 1G(T) | 30T
HDTV (4.3Mbps) | 1.8G | 20G(T) | Less 1P
3.3
If we can live a 120-year life (wish to every one), the information we read (write), speak (listen) and see could be:
Notes: POTS: Plain Old Telephone Servicing
POTS is characterized by several aspects:
Bi-directional (full duplex) communications.
Using balanced signaling of voltage analogs of sound pressure waves on a two-wire copper loops
Restricted to a narrow frequency range of 300 to 3300 Hz, called the voiceband, which is much less than the human hearing range of 20 - 20,000 Hz
Call-progress tones, such as dial tone and ringback tone.
Dial pulse signaling of addresses.
BORSCHT functions.
VHS: Video Home System (Lu Xiang Dai)

## Slide 36: Computer Systems Classification
Three general classes of “Computer”
  Desktop Computers
  Servers
  Embedded Computers
4.0

## Slide 37: Computer Systems-Desktop Computers
Examples include PC, Mac, Chrome, Linux…
Notebooks, netbooks, tablets (smart phones), …
Interact with users – applications
Handful of central processing units (4-12 CPUs), gigabytes (109 bytes) memory,
Few terabytes (1012 bytes) of disk
35 gigaflops (35×109 “floating-point math calculations” per second for Intel Ivy Bridge)
4.1

## Slide 38: Computer Systems-Servers
Web servers, Computational servers, Supercomputers
Interact with other computers to “solve a problem” or “provide services”
Dozens to thousands of CPUs (Tianhe-2: 3,120,000 CPUs, 33.9 petaflops, or 33.9×1015 calculations per second vs. 35×109 for PC)
Gigabytes to terabytes memory (Sequoia: 1,024,000GB [1.0 petabyte!])
Petabytes (1015 bytes) of storage
Connected (network) to work together
Power hungry but efficient (Tianhe-2: 17.8 MW vs. Three Mile Island ~800 MW output). Data centers: 1.7% to 2.2% of total electricity in US.)
4.2

## Slide 39: Computer Systems-Embedded Computers
Hidden inside something not computer
Applications that run on these computers interact with the “real world”
Multiple different processors for different functions
Kilobytes (103 bytes) to gigabytes of memory
Kilobytes to gigabytes of storage
Slow speed to fast speed
Widest range of design!
4.3

## Slide 40: The PostPC Era
4.4

## Slide 41: The PostPC Era
Personal Mobile Device (PMD)
  Battery operated
  Connects to the Internet
  Hundreds of dollars
  Smart phones, tablets, electronic glasses
Cloud computing
  Warehouse Scale Computers (WSC)
  Software as a Service (SaaS)
  Portion of software run on a PMD and a portion run in the Cloud
  Amazon and Google
4.4

## Slide 42: Computer systems: Commonality
Programmable: Software programs “run” on the hardware
Components
  Central processing unit (CPU): Does the computation
    A.k.a., “the processor”, “the core”
  Main memory: Temporarily holds results (volatile)
  Storage: Long term storage for large quantities
  Input/Output: Interaction (human, physical world or machine)
4.5

## Slide 43: Computer systems: Commonality
Von Neumann Machine
  Memory: Storage of information (data/program)
  Processing Unit: Computation/Processing of Information
  Input: Means of getting information into the computer
  Output: Means of getting information out of the computer
  Control Unit: Makes sure that all the other parts perform their tasks correctly and at the correct time.
4.5

## Slide 44: Computer systems: Commonality(Con.)
Metrics
  Speed: How fast computation is done. Faster is not always necessarily better. Usually some constraint/goal on speed.
  Energy/Power: A BIG concern today! Battery. Electricity cost and delivery to data center
4.5

## Slide 45: Why Computer Organization and Arch?
Why?
  A few people design processors/systems
  More people program on computers
  Every people uses computers!
5.0
The more you learn about the computer Organization and architecture, the higher efficiency you can achieve!

## Slide 46: Example-1
How to select a proper processor?
What are your concerns?
  Price?
  Performance?
  Reliability?
  CPU, Memory, Storage, GPU?
  …
5.0
Notes: Core number
Frequency
ISA
Cache
Memory
I/O

## Slide 47: Example-2
Map reduce programming
  System-1: 10 Xeon processors
  System-2: 80 ARM processors
  System-3: 10 Xeon + 80 ARM ??
5.0
Needs programming for system configuration

## Slide 48: What is Computer Arch
Broadest Definition
  Computer Architecture is the design the abstraction layers that allow us to implement information processing applications efficiently using available manufacturing technologies.
5.0
Application
Physics
Gap too Large to bridge in one single step

## Slide 49: Levels of Transformation
Microarchitecture
ISA (Architecture)
Program/Language
Algorithm
Problem
Logic
Circuits
Runtime System
(VM, OS, MM)
Electrons
“The purpose of computing is insight” (Richard Hamming)
We gain and generate insight by solving problems
How do we ensure problems are solved by electrons?
5.1
Notes: ISA is the interface between hardware and software… It is a contract that the hardware promises to satisfy.
Algorithm: step by step procedure where each step is effectively computable (by a computer), is definite (precisely defined) – “do until fast” is not definite, and terminates
Hamming distance: number of locations in which the corresponding symbols of two equal-length strings is different
Hamming, Richard W. (1950), "Error detecting and error correcting codes", Bell System Technical Journal 29 (2): 147–160
Hamming codes

## Slide 50: Aside: Papers By Hamming
Hamming, “Error Detecting and Error Correcting Codes,” Bell System Technical Journal 1950.
Introduced the concept of Hamming distance
  number of locations in which the corresponding symbols of two equal-length strings is different
Developed a theory of codes used for error detection and correction
Also:
Hamming, “You and Your Research,” Talk at Bell Labs, 1986.
  http://www.cs.virginia.edu/~robins/YouAndYourResearch.html
5.1

## Slide 51: The Power of Abstraction
Levels of transformation create abstractions
  Abstraction: A higher level only needs to know about the interface to the lower level, not how the lower level is implemented
  E.g., high-level language programmer does not really need to know what the ISA is and how a computer executes instructions
Abstraction improves productivity
  No need to worry about decisions made in underlying levels
  E.g., programming in Java vs. C vs. assembly vs. binary vs. by specifying control signals of each transistor every cycle
Then, why would you want to know what goes on underneath or above?
5.1

## Slide 52: Crossing the Abstraction Layers
As long as everything goes well, not knowing what happens in the underlying level (or above) is not a problem.
What if
  The program you wrote is running slow?
  The program you wrote does not run correctly?
  The program you wrote consumes too much energy?
What if
  The hardware you designed is too hard to program?
  The hardware you designed is too slow because it does not provide the right primitives to the software?
What if
  You want to design a much more efficient and higher performance system?
5.1

## Slide 53: How Do the Pieces Fit Together?
Coordination of many levels of abstraction
Under a rapidly changing set of forces
Design, measurement, and evaluation
5.1
I/O system
Instr. Set Proc.
Compiler
Operating
System
Application
Digital Design
Circuit Design
Instruction Set
Architecture
Firmware
Datapath & Control
Memory
system
S/W
H/W
Electron
Notes: For lecture

## Slide 54: What is ISA
5.2
I speak Spanish to God, Italian to women, French to men, and German to my horse.
Charles V, Holy Roman Emperor
(1500–1558)
… the portion of the machine visible to the programmer or compiler writer.
Hennessey and Patterson, 1990

## Slide 55: The Instruction Set: a Critical Interface
5.2
instruction set
software
hardware

## Slide 56: ISA & Computer Arch
By the architecture of a system, I mean the complete and detailed specification of the user interface. … As Blaauw has said, “Where architecture tells what happens, implementation tells how it is made to happen.”
The Mythical Man-Month, Brooks, pg 45
Computer Architecture = Instruction Set Architecture
+Machine Organization + …
5.2

## Slide 57: Levels of Representation
5.2
High Level Language Program
Assembly Language Program
Machine Language Program
Control Signal Specification
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
ALUOP[0:3] <= InstReg[9:11] & MASK

## Slide 58: Instruction Set Architecture
5.2
… the attributes of a (computing) system as seen by the programmer, i.e. the conceptual structure and functional behavior, as distinct from the organization of the data flows and controls the logic design, and the physical implementation.
Amdahl, Blaauw, and Brooks, 1964
SOFTWARE
-- Organization of Programmable
Storage
-- Data Types & Data Structures:
Encodings & Representations
-- Instruction Formats
-- Instruction (or Operation Code) Set
-- Modes of Addressing and Accessing Data Items and Instructions
-- Exceptional Conditions

## Slide 59: Computer Arch Contents
1950~1960s: Computer Arithmetic Logic Design
1970~1980s: Computer Instruction Set Arch Design
1990s: Computer Arch with multi sub-fields (e.g. Processor, Memory sys, I/O sys, Multi-processor, Networks, etc.)
Now: Extended Wilder and Deeper (e.g. Many(multi)-core processor, Hierarchical Memory, Fast I/O, Parallel processing, Network, SoC, Cloud Computing, DSA, etc.)
5.2

## Slide 60: Computer Arch Continually Changing
5.2
Applications
Technology
Compatibility
Applications suggest how to improve technology, provide revenue to fund development
Improved technologies make new applications possible
Cost of Software development makes compatibility a major force in market

## Slide 61: Definition of ISA
Instruction set architecture (ISA), is the part of the computer architecture related to programming, including the native data types, instructions, registers, addressing modes, memory architecture, interrupt and exception handling, and external I/O.
An ISA includes a specification of the set of opcodes (machine language), and the native commands implemented by a particular processor.
5.2

## Slide 62: Hardware/Software Interface: It Changes
DEC Alpha v1, v3 1992-97
HP PA-RISC v1.1, V2.0 1986-96
Sun Sparc v8, v9 1987-95
SGI MIPS MIPS I, II, III, IV, V 1986-96
Intel 8086, 80286, 80386, 1976-2013 80486, MMX, SSE, SSE2, SSE3, SSE4, x86-64, AVX, AES, AVX2&FMA, IA-64…
5.2
The line between hardware and software becomes somewhat fuzzy when last year’s software is embedded directly [for example] in read-only memory on a memory management chip where it is invisibly invoked by the programs being managed.
Harold Stone, 1987

## Slide 63: Computer Organization
The function and performance of the main units
  Registers, ALU, Shifter, Logic Unit, etc.
Interconnect among units
Communication among Units
Logic to control these information flows
Cooperating and running of functional units, in order to implement ISA.
Touch Register Transfer Level (RTL) Somehow!
  Recall Digital Circuit Design Please !!
5.3
SOFTWARE
From the view of Logic Design
ISA
Fun Units & Interconnect

## Slide 64: Computer Organization
Teardown happens in geeks’ life
5.3
RED = Apple APL1012 A8X 64-bit Processor ORANGE = Elpida (Micron Technology) F8164A3MD (two identical chips) YELLOW = SK Hynix H2JTDG8UD1BMR 128 Gb (16 GB) NAND Flash GREEN = NXP 65V10 NFC Module (as found in the iPhone 6 and 6 Plus) BLUE = Apple (Cirrus Logic) 338S1213 Audio Codec PURPLE = NXP Semiconductors LPC18B1UK ARM Cortex-M3 Microcontroller (Apple M8 Motion Co-Processor)
Notes: Tear the top glass panel off
Wifi Antennas
Touch ID biometric sensor
Speakers
Battery
Mainboard

## Slide 65: Computer Organization
Inside of Apple A8X

## Slide 66: Organization of Pentium 4
5.3

## Slide 67: Microarchitecture of Pentium 4
5.3

## Slide 68: Curriculum Subject
Why?
  Only few people design computer
  Everyone works with computer
    Knows more, works more efficiently
User-centered Computer System
  How to inspire users and be inspired by users
  Systematic consideration: Processer, Memory, I/O, Memory System, Network…
Benefits
  Design a faster program or design a program faster
  Chose hardware for specific APP.
  Know trends of tech (structure)
5.4
Computer Scientist and Engineer should know intrinsic characters of computer

## Slide 69: Curriculum Subject
Architecture Bridges from EE to CS
  What are the application requirements?
  What features are required to support OS?
  What features can optimizing compilers use?
  What hardware can I build?
  What hardware can I build next year?
Computer Arch must be broad!
5.4

## Slide 70: Overview of Physical Implementations
Integrated Circuits (ICs)
  Combinational Logic Circuits, Memory Elements, analog Interfaces
Printed Circuits (PC) Boards
  Substrate for ICs and Interconnections, Distribution of CLK, Vdd, and GND Signals, Heat Dissipation.
Power Supplies
  Converts Line AC voltage to regulated DC low voltage levels.
Chassis (Rack, Card Case, …)
  Holds Boards, Power Supply, Provides Physical Interface to user or other systems
Connectors and Cables
5.5
The hardware out of which we makes systems.

## Slide 71: Integrated Circuits
Silicon Chips
1mm-25mm on a side
Feature size ~14nm =14x10-9m (2016)
Max10B transistors
More than 10 metal layers
CMOS (Complementary Metal Oxide Semiconductor) -most common
5.5
Package Provides:
  Bonding wires from chip to board (signal paths)
  heat dissipation
Ceramic or plastic (strengthening with metal for military standard) with gold wires
Notes: ProcessorTransistor countDate of introductionDesignerProcessArea
Intel 40042,3001971Intel10,000 nm12 mm²
Intel 80083,5001972Intel10,000 nm14 mm²
Intel 80804,5001974Intel6,000 nm20 mm²
IBM z13 Storage Controller7,100,000,0002015IBM22 nm678 mm²
IBM z133,990,000,0002015IBM22 nm678 mm²
Quad-core + GPU GT2 Core i7 Skylake K1,750,000,0002015Intel14 nm122 mm²
Duo-core + GPU Iris Core i7 Broadwell-U1,900,000,000[23]2015Intel14 nm133 mm²
SPARC M710,000,000,000[33]2015Oracle20 nm
Apple A10 (quad-core ARM64 "mobile SoC")3,300,000,0002016Apple16 FFC125 mm²
22-core Xeon Broadwell-E57,200,000,000[32]2016Intel14 nm456 mm²

## Slide 72: Printed Circuit Boards
FR-4 Glass Epoxy
1-20 conductive layers
IC packages are soldered down
Provides:
  Mechanical support
  Distribution of power and heat
5.5

## Slide 73: Moore’s Law & Others
Moore’s law
  However it dying or has been dead.
  Intel Cannonlake and 10nm are still planned but are not due until the second half of 2017
5.6
Gordon Moore's original graph, showing projected transistor counts, long before the term "Moore's law" was coined.

## Slide 74: Moore’s Law & Others
2x Transistors /Chip Every 1.5 years
Called “Moore’s Law”
5.6
Gordon Moore
Intel Cofounder

## Slide 75: Moore’s Law & Others
Moore’s Law
5.6
Gordon Moore
Intel Cofounder

## Slide 76: Moore’s Law & Others
Memory Capacity (Single-Chip DRAM)
5.6
1.4X/yr,  2X every 2 yrs  Much Lower Now (12Gbit to 16Gbit LPDDR4 takes 14 months in Samsung)
80XX since 1980!
Year Size
1980 0.0625Mbit
1983 0.25Mbit
1986 1Mbit
1989 4Mbit
1992 16Mbit
1996 64Mbit
1998 128Mbit
2000 256Mbit
2002 512Mbit
2004 1Gbit
2006 2Gbit
2009 4Gbit
…
2014 12Gbit
2016 16Gbit
Programmer interested on small memory optimization, 30 years ago.

## Slide 77: Moore’s Law & Others
35 years of Microprocessor Trend
5.6
Single-thread Performance trend changes
  VAX: 1.25x/y 1978 to 1986
  RISC+x86: 1.52x/y 1986 to 2002
  RISC+x86: 1.20x/y 2002 to 2006
  Single-thread Performance growth keeps slowing down now
Programmer interests on parallelism NOW
no mater in PMD, Cloud Computing, or SaaS.

## Slide 78: Moore’s Law & Others
Energy Efficiency
  Surging demand for new products and the continuing existence of inefficient products will drive energy use up
  Increased energy use is raising energy costs and causing haze weather.
  Energy efficiency will drive demand for new products
5.6

## Slide 79: Moore’s Law & Others
Computer Technology – Dramatic Changes!
  Memory
    DRAM Capacity: 2x / 2 years (since 1996)
      64x size improvement in last decade
  Processor
    Speed 2x / 1.5 years (since 1985) [slowing down]
      100x performance in last decade
  Disk
    Capacity: 2x / year (since 1997)
      250x size in last decade
5.6

## Slide 80: Moore’s Law & Others
Computer Technology – Dramatic Changes!
  State-of-the-art PC when you graduate:
    Processor clock speed: 4,000 Mega Hertz (4.0 Giga Hertz)
    Memory capacity: 65,536 Mebi Bytes (64.0 Gibi Bytes)
    Disk Capacity: 4,000 Giga Bytes (4.0 Tera Bytes)
    Units! Mega => Giga, Giga => Tera (Tera => Peta, Peta => Exa, Exa => Zetta, Zetta => Yotta = 1024)
5.6
You just learned the difference between (Kilo, Mega, …) and (Kibi, Mebi, …)!

## Slide 81: Moore’s Law & Others
Decades | Minimum Price | Features
60s | $millions | Mainframes Computers
70s | $10K-100K | Minicomputer
80s | $10K | Workstations & PCs
90s | $1K | Internet PCs
00s | $100s | PDA, Cell Phones
10s | $10 | Tablets, Clouds, Wearable,…
?? | ? | Carbon, DNA, Quantum, Bio?
5.6
A new class emerges and some die every decade.
Bell’s Law of Computer Classes
New Computer  New Applications  Emerging Industries

## Slide 82: Moore’s Law & Others
5.6
A new class emerges and some die every decade.
Bell’s Law of Computer Classes
New Computer 
New Applications 
Emerging Industries

## Slide 83: Moore’s Law & Others
5.6
Software is a gas!
It expands to fit the container it is in!
Nathan’s 1st Law of Sftware (ACM97)

## Slide 84: Moore’s Law & Others
Initial growth is rapid – like gas expanding (like browser)
Eventually, limited by hardware (like NT)
Bring any processor to its knees, just before the new model is out
5.6
Software grows until it becomes limited by Moore’s Law
Nathan’s 2nd Law of Sftware (ACM97)

## Slide 85: Moore’s Law & Others
That’s why people buy new hardware – economic motivator
That’s why chips get faster at same price, instead of cheaper
Will continue as long as there is opportunity for new software
5.6
Software growth makes Moore’s Law possible
Nathan’s 3rd Law of Sftware (ACM97)

## Slide 86: Moore’s Law Goes with Software
Hardware update, driven by the requirement of New Software
Processor price keeps steady, no Inc, no Dec, however performance improved.
If software companies stop updating, the hungering of processor performance will be stop.

## Slide 87: Moore’s Law & Others
It’s impossible to have enough for human
    Socrates said He who is not contented with what he has, would not be contented with what he would like to have.
New algorithms
New applications and new users
New notions of what is cool
5.6
Software is only limited by human ambition & expectation
Nathan’s 4th Law of Software (ACM97)

## Slide 88: What happened in last 3-decade
Performance
  Improvement of Fabrication Technology
    CMOS VLSI outperformances Old-Tech (TTL, ECL)
  Improvement of Computer Architecture
    RISC, Superscalar, RAID, etc.
  Leverage Low-end Products
    ARM, MCU

## Slide 89: Measurement & Evaluation
Design
Analyze
Architecture Study follows the iterations
The Iteration happens in any hierarchic levels
Design Space Exploration happens in any design corner.
Design Space
Cost/Perfor-mance
Design Space
Convergence
Bad Idea
Not that Bad
Good Idea
Creativity

## Slide 90: Content Structure
Computer Organization & Architecture
ISA & System Design
Interfaces
from the view of compiler /System
“Building Architect”
Computer Organization
Hardware
from the view of logical designer
“Construction Engineer”

## Slide 91: Content Structure – more Secular & Utility
Computer Organization & Architecture
ISA & System Design
Interfaces
Machine Language
From the view of compiler /System
Computer Architecture
Instruction System & Processor
“Building Architect”
Computer Organization
Hardware
Machine Implementation
From the view of logical designer
Architecture of Processor
Computer Organization
“Construction Engineer”
Little amount of people work with Computer Design! Much less with ISA Design!
Large amount of people work with Computer Components Design…
Much more care about the detailed Functionality of Computer…

## Slide 92: Content levels
Diagram of Representations
High Level Language Program
Assembly Language Program
Machine Language Program
Control Signal Specification
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
ALUOP[0:3] <= InstReg[9:11] & MASK

## Slide 93: Content levels
Diagram of Representations
5.6
High Level Language Program
Assembly Language Program
Machine Language Program
Control Signal
Specification
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Hardware Arch Description
(e.g. block diagrams)
Logic Circuit Description
(e.g. Circuit Schematic)

## Slide 94: Recall the First Example
200x speedup for matrix vector multiplication
Data level parallelism(DLP, SIMD): 3.8x (Ch. 3)
Loop unrolling and out-of-order execution， Instruction Level Parallelism(ILP):2.3x (Ch.4)
Cache blocking, Memory Hierarchy Optimization: 2.5x (Ch. 5)
Thread Level Parallelism, parallel for loops in Multicore systems: 14x (Ch. 6)
Further, can use accelerators to get an additional 100x.
5.6

## Slide 95: Course Goal
Answer 7 Questions (Blue for S Designers, Red for H Designers)
  How are programs translate into hardware language and how does it execute?
    To build the concepts of program performance impacted by both S/H
  What is the interface between Soft/Hardware and how software instruct hardware to perform functions?
    To build understanding of writing many kinds of programs
  What determines the performance of a program and how to improve it?
    Effectiveness
  What techniques can be used to improve performance?
    Only basic concepts in this course, more advanced are on Computer Arch
  What techniques can be used to improve energy efficiency? What can programmers do in energy efficiency?
  What are reasons and consequences of parallelism?
    Mainly multicore
  What great ideas of computer architecture lay the foundation of modern computing

## Slide 96: Course Goal
Understanding: Internal mechanism, developing features, and the trade-off, between Software and Hardware, of modern computer
  Can observe which operation fast/slow, can also understand which implementation hard/easy in hardware
  “Taste” the design flow via large, complicate (hardware) system
  Know the flow
    Function description => Control & Data Path => Transistor (Phisics)
  Understand the concept of IC Design and CAD (Computer-aided Design)
Skill Tree of IT Designer

## Slide 97: Skill Tree
Evaluation Techniques
Levels of Translation (e.g. compilation)
Levels of Interpretation (e.g. Microprogramming)
Hierarchy (e.g. registers, cache, mem, disk, tape)
Pipelining and Parallelism
Static/Dynamic Scheduling
Indirection and Address Translation
Synchronous and Asynchronous Control Transfer
Timing, Clocking, and Latching
Physical Design of Cells (e.g. CLA)
Understanding Technology and Foundary Developing
……
Notes: 评测技术
变换的级别
解释的级别
层次化
流水和并行
静态／动态调度
间址和地址变换
同步和异步传输
时序、时钟同步、锁存
单元的物理设计
技术工艺发展趋势

## Slide 98: Summary Although Different with Textbook
Three general classes of “Computer”
Computer systems: Commonality
Computer Architecture: Abstraction
ISA
Computer Organization
6

## Slide 99: Goal of CH. 1
Basic Idea and Definitions
  1.1 ~ 1.2
Major components of software and hardware in perspective
  1.3 ~ 1.4
How to evaluate performance and energy (next slides)
  1.6 ~ 1.7, 1.9
IC Introduction (that fuels the computer revolutions, next slides, partially)
  1.5
The shift to multicores
  1.8

## Slide 100: Reading Assignment
Extension Reading
  1.12 Historical Perspective and Further Reading
    Available online