## Slide 1: Lecture1 Introduction (III) Cost & Performance Metrics
Computer Organization and Architecture

## Slide 2: The chip manufacturing process
1.0
Yield: proportion of working dies per wafer

## Slide 3: Intel Core i7 Wafer
300mm wafer, 280 chips, 32nm technology
Each chip is 20.7 x 10.5 mm

## Slide 4: Cost of ICs

## Slide 5: Other Costs
Packing Cost: Depends on the pin number and the requirement of heat dissipation

## Slide 6: Cost / Performance
Component Costs
Direct Costs (add 25% to 40%) recurring costs: labor, purchasing, scrap, warranty
Gross Margin(add 82% to 186%) nonrecurring costs: R&D, marketing, sales, equipment maintenance, rental, financing cost, pretex profits, taxes
Average Discount to get list Price (add 33% to 66%): volume discounts and/or retailer markup
2.0
What is the relationship between Cost and Price?

## Slide 7: Profit from Margin in Hardware -- Apple

## Slide 8: How to Define the Performance
Different architectures
Different implementations of an architecture
Different compilers for a given architecture
The goal of performance evaluation in this chapter is to be able to compare, for example.
General Sense:
How well the computer performs?

## Slide 9: Defining Performance
Which airplane has the best performance?

## Slide 10: Performance and cost
Airplane | Washington -Paris | Speed | Passengers | Through-put
Boeing 747 | 6.5 hours | 610 mph | 470 | 286,700
BAD/Sud Concodre | 3 hours | 1350 mph | 132 | 178,200
Time to execute a task (Execution Time)
  Execution time, response time, latency
Tasks that executed in a unit time( per day, per hour, per week, per second,…) (Performance)
  Throughput, bandwidth

## Slide 11: Throughput and response time
How will the throughput and response time be influenced if :
  Use a more faster processor?
  Use more processors and assign different task to different processor?
Reducing response can always improve throughput!
Response time of a task can not be improved with more processors, if the task can not be parallelized!
In real systems, tasks usually need to wait in line for execution, execution time and throughput usually affect each other.

## Slide 12: Defining (Speed) Performance
Normally interested in reducing
  Response time (aka execution time) – the time between the start and the completion of a task
    Important to individual users
  Thus, to maximize performance, need to minimize execution time
  Throughput – the total amount of work done in a given time
    Important to data center managers
  Decreasing response time almost always improves throughput
performanceX = 1 / execution_timeX
  If X is n times faster than Y, then
performanceX execution_timeY
-------------------- = --------------------- = n
performanceY execution_timeX
Notes: Increasing performance requires decreasing execution time

## Slide 13: Metrics of performance
Response per month
Operations per second
Application
Program Language
Complier
Datapath
Control
Functional Units
Trans. Wire, Pin

## Slide 14: The Nature of Time
Unless otherwise specified, “time” often refers to “user time”

## Slide 15: Executing Time
Elapsed Time
  Counts everything (disk and memory accesses, I/O, etc.)
  A useful parameter, but often not for comparing purposes
CPU Time
  No counts I/O and time running other programs
  Can be separated into System Time, and User Time
Our focus: user CPU time
  Executing the lines of code that are “in” our program

## Slide 16: Time
Wall-clock time, response time, or elapsed time: the total time to complete a task, including disk accesses, memory accesses, input/output activities, operating system overhead. — everything!
CPU execution time or CPU time: the time CPU spends computing for a specific task with no counting the waiting time of I/O or running other programs.

## Slide 17: CPU Time
If we know # of CPU clock cycles for a program
  CPU time for a program
  = # of CPU cycles for a program X Clock cycle time
  = # of CPU cycles for a program / Frequency
  (period per cycle)

## Slide 18: Performance Factors
Want to distinguish elapsed time and the time spent on our task
CPU execution time (CPU time) – time the CPU spends working on a task
  Does not include time waiting for I/O or running other programs
Can improve performance by reducing either the length of the clock cycle or the number of clock cycles required for a program
# of CPU clock cycles for a program
= # of instructions of a program
X
average clock cycles for an instruction
Notes: Many techniques that decrease the number of clock cycles also increase the clock cycle time

## Slide 19: Clock Cycles per Instruction
Not all instructions take the same amount of time to execute
  One way to think about execution time is that it equals the number of instructions executed multiplied by the average time per instruction
Clock cycles per instruction (CPI) – the average number of clock cycles each instruction takes to execute
  A way to compare two different implementations of the same ISA

## Slide 20: Quiz
A compiler writer needs to determinate from 2 code sequences
  Hardware performance fact for 3 classes of Instruction:
  Two code sequences below:
  Cycle1=(2x1)+(1x2)+(2x3)=10 Cycle2=(4x1)+(1x2)+(1x3)=9
  CPI1=10/5=2 CPI2=9/6=1.5
 | CPI for this instruction class |  | 
 | A | B | C
CPI | 1 | 2 | 3
Seq. # | Instruction count for each class |  | 
 | A | B | C
1 | 2 | 1 | 2
2 | 4 | 1 | 1

## Slide 21: The Performance Equation
Our basic performance equation is then
CPU time = Instruction_count x CPI x clock_cycle
These equations separate the three key factors that affect performance
  Can measure the CPU execution time by running the program
  The clock rate is usually given
  Can measure overall instruction count by using profilers/ simulators without knowing all of the implementation details
  CPI varies by instruction type and ISA implementation for which we must know the implementation details
Notes: Note that instruction count is dynamic – i.e., its not the number of lines in the code, but THE NUMBER OF INSTRUCTIONS EXECUTED

## Slide 22: Determinates of CPU Performance
 | Instruction_count | CPI | clock_cycle
Algorithm |  |  | 
Programming language |  |  | 
Compiler |  |  | 
ISA |  |  | 
Processor organization |  |  | 
Technology |  |  | 
CPU time = Instruction_count x CPI x clock_cycle
X
X
X
X
X
X
X
X
X
X
X
X
Notes: For lecture

## Slide 23: Effective CPI
Computing the overall effective CPI is done by looking at the different types of instructions and their individual cycle counts and averaging
Overall effective CPI =  (CPIi x ICi)
i = 1
n
  Where ICi is the count (percentage) of the number of instructions of class i executed
  CPIi is the (average) number of clock cycles per instruction for that instruction class
  n is the number of instruction classes
The overall effective CPI varies by instruction mix – a measure of the dynamic frequency of instructions across one or many programs

## Slide 24: A Simple Example
Op | Freq | CPIi | Freq x CPIi
ALU | 50% | 1 | 
Load | 20% | 5 | 
Store | 10% | 3 | 
Branch | 20% | 2 | 
 |  |  |  =
0.5
1.0
0.3
0.4
2.2
How much faster would the machine be if a better data cache reduced the average load time to 2 cycles?
How does this compare with using branch prediction to shave a cycle off the branch time?
What if two ALU instructions could be executed at once?

## Slide 25: A Simple Example
How much faster would the machine be if a better data cache reduced the average load time to 2 cycles?
How does this compare with using branch prediction to shave a cycle off the branch time?
What if two ALU instructions could be executed at once?
Op | Freq | CPIi | Freq x CPIi
ALU | 50% | 1 | 
Load | 20% | 5 | 
Store | 10% | 3 | 
Branch | 20% | 2 | 
 |  |  |  =
.5
1.0
.3
.4
2.2
CPU time new = 1.6 x IC x CC so 2.2/1.6 means 37.5% faster
1.6
.5
.4
.3
.4
.5
1.0
.3
.2
2.0
CPU time new = 2.0 x IC x CC so 2.2/2.0 means 10% faster
.25
1.0
.3
.4
1.95
CPU time new = 1.95 x IC x CC so 2.2/1.95 means 12.8% faster
Notes: For lecture

## Slide 26: Benchmark Suites
Each vendor announces a SPEC rating for their system
  a measure of execution time for a fixed collection of programs
  is a function of a specific CPU, memory system, IO system, operating system, compiler
  enables easy comparison of different systems
The key is coming up with a collection of relevant programs

## Slide 27: Benchmarks
SPEC: System Performance Evaluation Corporation, an industry consortium that creates a collection of relevant programs (SPEC Series (http://www.spec.org)
The 2006 version includes 12 integer and 17 floating-point applications
The SPEC rating specifies how much faster a system is, compared to a baseline machine – a system with SPEC rating 600 is 1.5 times faster than a system with SPEC rating 400
Note that this rating incorporates the behavior of all 29 programs – this may not necessarily predict performance for your favorite program!
PARSEC (http://parsec.cs.princeton.edu/)
The Princeton Application Repository for Shared-Memory Computers (PARSEC) is a benchmark suite composed of multithreaded programs.
Others
SPLASH, BioPef, Biobench, TPC-C/H …

## Slide 28: Comparing and Summarizing Performance
Guiding principle in reporting performance measurements is reproducibility – list everything another experimenter would need to duplicate the experiment (version of the operating system, compiler settings, input set used, specific computer configuration (clock rate, cache sizes and speed, memory size and speed, etc.))
How do we summarize the performance for benchmark set with a single number?
  The average of execution times that is directly proportional to total execution time is the arithmetic mean (AM) (What else?)
AM = 1/n  Timei
i = 1
n
  Where Timei is the execution time for the ith program of a total of n programs in the workload
  A smaller mean indicates a smaller average execution time and thus improved performance

## Slide 29: Comparing and Summarizing Performance
How do we summarize the performance for benchmark set with a single number?
  SPEC uses geometric mean (GM) – the execution time of each program is multiplied and the Nth root is derived
  Weighted arithmetic mean – the execution times of some programs are weighted to balance priorities

## Slide 30: 不同平均值的对比
Notes: 参考资料：https://blog.csdn.net/ecnu18918079120/article/details/71307845

## Slide 31: Evaluating ISAs
Design-time metrics:
  Can it be implemented, in how long, at what cost?
  Can it be programmed? Ease of compilation?
Static Metrics:
  How many bytes does the program occupy in memory?
Dynamic Metrics:
  How many instructions are executed? How many bytes does the processor fetch to execute the program?
  How many clocks are required per instruction?
  How "lean" a clock is practical?
Best Metric: Time to execute the program!
CPI
Inst. Count
Cycle Time
depends on the instructions set, the processor organization, and compilation techniques.

## Slide 32: MIPS vs MIPS
MIPS: Originally for Microprocessor without Interlocked Pipeline Stages ( Arch Acronym)
MIPS: Million Instructions per Second (Performance Acronym)

## Slide 33: Other Metrics: Power Consumption
Back to 70’s ~ 80’s, designers only cared about performance
  Now, the story has changed…
Power consumption – especially in the embedded market where battery life is important (and passive cooling)
  For power-limited applications, the most important metric is energy efficiency
Pentium |  | 200 MHz | 15.5 W
Pentium II 450 | Deschutes (250 nm) | 450 MHz | 27.1 W
Pentium III 1400S | Tualatin (130 nm) | 1.4 GHz | 32.2 W
Haswell High-End | Sandybridge-E (32 nm) | 3.3 GHz @ 6 Cores | 130 W

## Slide 34
Notes: 参考资料：jianshu.com/p/243d0d9cd2fe

## Slide 35: Two Types of Energy Consumption
Capacitors dominate dynamic energy (primary energy consumption)
Static energy consumes even if transistors are always off
  Leakage is typical responsible for > 40% energy consumption.
Energy ∝ Capacitive load x Voltage2
Energy ∝ 1/2 x Capacitive load xVoltage2
Power ∝ 1/2 x Capacitive load x Voltage2 x Frequency switched
Notes: 参考资料：https://www.jianshu.com/p/2f6aa8adac7a
现在的设计普遍认为，功耗密度高于150W/c㎡是应该极力避免的，除非说你完全不在乎封装的成本。
根据估算，在20nm工艺下，以前的45nm处理器如果采用1.2V供电，不考虑散热的话，其实运行频率理论上可以达到30GHZ。但是带来的问题就是功耗密度达到惊人的20KW/c㎡，远高于太阳表面的功耗密度。即便运行频率达到10GHZ，功耗密度也达到5KW/c㎡，比火箭的尾焰还热。所以从散热考虑，实际的处理器运行频率都被限制在10GHZ以内，即便晶体管的速度允许其达到10GHZ。

## Slide 36: Example Problem
A 1 GHz processor takes 100 seconds to execute a program, while consuming 70 W of dynamic power and 30 W of leakage power. Does the program consume less energy in Turbo boost mode when the frequency is increased to 1.2 GHz?

## Slide 37
超频运行会使得该程序执行的总能耗如何改变？
增加
不变
降低
A
B
C
提交
投票
最多可选1项
D
不一定

## Slide 38: Example Problem
A 1 GHz processor takes 100 seconds to execute a program, while consuming 70 W of dynamic power and 30 W of leakage power. Does the program consume less energy in Turbo boost mode when the frequency is increased to 1.2 GHz?
Normal mode energy = 100 W x 100 s = 10,000 J
Turbo mode energy = (70 x 1.2 + 30) x 100/1.2 = 9,500 J
Note:
Frequency only impacts dynamic power, not leakage power.
We assume that the program’s CPI is unchanged when
frequency is changed, i.e., exec time varies linearly
with cycle time.
Notes: 此处可以打开任务管理器，看基准频率与实时速度

## Slide 39: DARK Silicon
We come to a utilization wall which says that with the progression of Moore's Law, the percentage of a chip that we can actively use within a chip's power budget is dropping exponentially! The remaining silicon that must be left unpowered is now referred to as Dark Silicon.
--UCSD Dark Silicon Team
Notes: Tbyte = 2^40 bytes (or 10^12 bytes)
Note that Moore’s law is not about speed predictions but about chip complexity

## Slide 40
Notes: 参考资料：https://www.jianshu.com/p/2f6aa8adac7a

## Slide 41: Power of Supercomputers
Notes: 参考网站：www.top500.org
播放视频：申威处理器简介

## Slide 42: How about Data Centers?
  “Data centers consumes up to 1.5% of all the world’s electricity”
  “Google’s data centers draw almost 260 MW of power, which is more power than Salt Lake City uses.”

## Slide 43: Other Metrics: Reliability
Sources of Errors
  Particle-strike soft errors
  Negative bias temperature instability (NBTI)
  Electron-migration
  Power failure
  …
Protection mechanisms
  Error correction codes
  Redundant logic
  Checkpoint, duplication …
Trade-off
  Reliability ↑  Design overhead (complex) ↑  Performance ↓
  Reliability ↑  Design overhead / Function activity ↑  Power ↑

## Slide 44: Typical Server System Reliability Goals
Error Type | System MTBF Goal
SDC (Silent Data Corruption) | 1000 years
DUE for system crash | 25 years
DUE for application crash | 10 years
(D.C.Bossen, 2002 IRPS Tutorial Reliability Notes)
SDC = Silent Data Corruption
DUE = Detected & unrecoverable error
MTBF = mean time before failure
Notes: Transition: Now we will see how our rates match up against these goals and requirements.

## Slide 45: Amdahl’s Law
Slatency: the theoretical speedup of the execution of the whole task
s : speedup of the part of the task that benefits from improved resources
p is the proportion of execution time that the part benefiting from improved resources originally occupied.
Architecture design is very bottleneck-driven – make the
common case fast, do not waste resources on a component
that has little impact on overall performance/power
Amdahl‘s law（阿姆达尔定律） 由计算机科学家 Gene Amdahl 在 1967 年提出，主要思想是当我们对系统的某个部分加速时，其对系统整体性能的影响取决于该部分的所占比例和加速程度

## Slide 46: Amdahl’s Law
Example: a web server spends 40% of time in the CPU and 60% of time doing I/O – a new processor that is ten times faster results in a 36% reduction in execution time (4%+60%)
(speedup of 1.56) – Amdahl’s Law states that maximum execution time reduction is 40% (max speedup of 1.66)

## Slide 47: Next Lecture and Reminders
Next lecture
  ISA Review
    Reading assignment – PH, Chapter 2