## Slide 1: Lecture4 ISA Basic
Computer Organization and Architecture

## Slide 2: Outline
Functional Design of Instruction Set
  a.k.a. ISA Basic (Today’s Topic) (2.1~2.5)
More ISA
  Detailed ISA, Endian-ness, Addressing, CISC vs RISC
More Detailed MIPS ISA
    Types of MIPS ISA, Procedure call, Programming with MIPS Assembly
0.0

## Slide 3: Function Design of Instruction Set
1.0
ADD 01010
SUBTRACT 01110
AND 10011
OR 10001
COMPARE 11010
. .
. .
. .
Programmer’s View
Computer’s View
Princeton ( Von Neumann) Architecture
Uses the same memory & data paths for both Instructions & Data storage.
  “Stored Program Computer”
High efficient Storage Utilization at large scale application
Unified Memory Port
CPU
I/O
Memory
Program
(Instructions)

## Slide 4: Function Design of Instruction Set
1.0
ADD 01010
SUBTRACT 01110
AND 10011
OR 10001
COMPARE 11010
. .
. .
. .
Programmer’s View
Computer’s View
Princeton ( Von Neumann) Architecture
Uses the same memory & data paths for both Instructions & Data storage.
  “Stored Program Computer”
High efficient Storage Utilization at large scale application
Unified Memory Port
Harvard Architecure
Uses physically separate memory & data paths for Instructions & Data memory.
    “Stored Program Computer”
Still works well at the small scale, DSP, MCU, e.g. Arduino (Atmel MCU)

## Slide 5: Execution Cycle of Instruction
Instruction Format or Encoding
  how is it decoded?
Location of operands and result
  where other than memory?
  how many explicit operands?
  how are memory operands located?
  which can or cannot be in memory?
Data type and Size
Operations
  what are supported
Successor instruction
  jumps, conditions, branches
  fetch-decode-execute is implicit!
1.1
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 6: A Basic MIPS Instruction
C code: a = b + c ;
Assembly code: (human-friendly machine instructions)
add a, b, c # a is the sum of b and c
Machine code: (hardware-friendly machine instructions)
00000010001100100100000000100000
Translate the following C code into assembly code:
a = b + c + d + e;
Notes: Words to the right of the sharp symbol (#) on each line above are comments
for the human reader, so the computer ignores them.

## Slide 7: Example
C code a = b + c + d + e;
translates into the following assembly code:
add a, b, c add a, b, c
add a, a, d or add f, d, e
add a, a, e add a, a, f
Instructions are simple: fixed number of operands (unlike C)
A single line of C code is converted into multiple lines of assembly code
Some sequences are better than others… the second sequence needs one more (temporary) variable f

## Slide 8: Subtract Example
C code f = (g + h) – (i + j);
Assembly code translation with only add and sub instructions:

## Slide 9: Subtract Example
C code f = (g + h) – (i + j);
Assembly code translation with only add and sub instructions:
add t0, g, h add f, g, h
add t1, i, j or sub f, f, i
sub f, t0, t1 sub f, f, j
Each version may produce a different result because
floating-point operations are not necessarily
associative and commutative… more on this later

## Slide 10: Instruction Format
The OPCOD defines the operation of the instruction, such as addition, subtraction, data transfer, etc.
The OPERANDs designate the operate object of the OPCOD, which are the index of the register file, the address of memory, etc.
Both the OPCOD and OPERAND are represented in binary.
1.2
OPCOD
OPERAND
OPERAND
…

## Slide 11: Operands
In C, each “variable” is a location in memory
In hardware, each memory access is expensive – if variable a is accessed repeatedly, it helps to bring the variable into an on-chip scratchpad and operate on the scratchpad (registers)
To simplify the instructions, we require that each instruction (add, sub) only operate on registers (for MIPS)
Note: the number of operands (variables) in a C program is very large; the number of operands in assembly is fixed… there can be only so many scratchpad registers

## Slide 12: Registers
The MIPS ISA has 32 registers (x86 has 8 registers) – Why not more? Why not less?
Each register is 32-bit wide (modern 64-bit architectures have 64-bit wide registers)
A 32-bit entity (4 bytes) is referred to as a word
To make the code more readable, registers are partitioned as $s0-$s7 (C/Java variables), $t0-$t9 (temporary variables)…

## Slide 13: Memory Operands
Values must be fetched from memory before (add and sub) instructions can operate on them
Load word
lw $t0, memory-address
Store word
sw $t0, memory-address
How is memory-address determined?
Register
Memory
Register
Memory

## Slide 14: Memory Address
The compiler organizes data in memory… it knows the location of every variable (saved in a table)… it can fill in the appropriate mem-address for load-store instructions MIPS (almost all ARCHs today) addresses each byte, word addresses are multiples of 4; 32-bit int 4 bytes
Memory
…
Base address
int a, b, c, d[10]

## Slide 15: Immediate Operands
An instruction may require a constant as input
An immediate instruction uses a constant number as one of the inputs (instead of a register operand)
Putting a constant in a register requires addition to register $zero (a special register that always has zero in it) -- since every instruction requires at least one operand to be a register
For example, putting the constant 1000 into a register:
addi $s0, $zero, 1000

## Slide 16: Example
addi $s0, $zero, 1000 # the program has base address
# 1000 and this is saved in $s0
# $zero is a register that always
# equals zero
addi $s1, $s0, 0 # this is the address of variable a
addi $s2, $s0, 4 # this is the address of variable b
addi $s3, $s0, 8 # this is the address of variable c
addi $s4, $s0, 12 # this is the address of variable d[0]

## Slide 17: Memory Instruction Format
The format of a load instruction:
destination register
source address
lw $t0, 8($t3)
any register
a constant that is added to the register in brackets

## Slide 18: Memory Instruction Format
The format of a store instruction:
source register
destination address
sw $t0, 8($t3)
any register
a constant that is added to the register in brackets

## Slide 19: Example
Convert to assembly:
C code: d[3] = d[2] + a;

## Slide 20: Example
Convert to assembly:
C code: d[3] = d[2] + a;
Assembly: # addi instructions as before
lw $t0, 8($s4) # d[2] is brought into $t0
lw $t1, 0($s1) # a is brought into $t1
add $t0, $t0, $t1 # the sum is in $t0
sw $t0, 12($s4) # $t0 is stored into d[3]
Assembly version of the code continues to expand!

## Slide 21: Basics of Instruction Design
Software and hardware are logically equal.
Architecture decides which functional will be implemented by instructions. Three characteristics should be taken into consideration:
  Speed
  Cost
  Flexibility
1.3

## Slide 22: Basics of Instruction Design
Which operation should be provided? How many operation should be provided?
  A instruction set with only LD/ST/INC/BRN is enough.
  But it is not practical. Why?
How to designate the operands? How many operand can be inferred by a instruction?
  Most of the operations are dyadic(双值运算) (A<=A+B)
  Some are monadic(单值运算）(A<=~B)
How to encode all these instructions into a formal format?
Challenge: How to encode the operation in less bits?
1.3

## Slide 23: Recap – Numeric Representations
Decimal 3510 = 3 x 101 + 5 x 100
  D to B
Binary 001000112 = 1 x 25 + 1 x 21 + 1 x 20
  B to D
Hexadecimal (compact representation)
0x 23 or 23hex = 2 x 161 + 3 x 160
0-15 (decimal)  0-9, a-f (hex)
Dec Binary Hex
0 0000 00
1 0001 01
2 0010 02
3 0011 03
Dec Binary Hex
4 0100 04
5 0101 05
6 0110 06
7 0111 07
Dec Binary Hex
8 1000 08
9 1001 09
10 1010 0a
11 1011 0b
Dec Binary Hex
12 1100 0c
13 1101 0d
14 1110 0e
15 1111 0f
  3510
  001000112
  100111002
  15610

## Slide 24: Singed and Unsinged
Negation Shortcut
  2ten 0000 0000 0000 0000 0000 0000 0000 0010two
  Negating this number by inverting all bits and adding 1
  Vice versa
0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
0000 0000 0000 0000 0000 0000 0000 0001two = 1ten
... ... 0111 1111 1111 1111 1111 1111 1111 1110two = 2,147,483,646ten
0111 1111 1111 1111 1111 1111 1111 1111two = 2,147,483,647ten
1000 0000 0000 0000 0000 0000 0000 0000two = –2,147,483,648ten
1000 0000 0000 0000 0000 0000 0000 0001two = –2,147,483,647ten
... ... 1111 1111 1111 1111 1111 1111 1111 1101two = –3ten
1111 1111 1111 1111 1111 1111 1111 1110two = –2ten
1111 1111 1111 1111 1111 1111 1111 1111two = –1ten

## Slide 25: MIPS Instruction Format
Instructions are represented as 32-bit numbers (one word),
broken into 6 fields (or 4 fields)
R-type instruction add $t0, $s1, $s2
I-type instruction lw $t0, 32($s3)
Compromise， length vs format
6 bits | 5 bits | 5 bits | 16 bits
opcode | rs | rt | constant
000000 | 10001 | 10010 | 01000 | 00000 | 100000
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | rd | shamt | funct
opcode | reg source | reg source | reg dest | Shift amt | function

## Slide 26: MIPS Instruction Format
Instructions are represented as 32-bit numbers (one word),
broken into 6 fields (or 4 fields)
And J-type instruction Jump more detailed later
R-type
I-type

## Slide 27: Basic Requirements of Instruction Set
Integrity
Regularity
Efficiency
Compatibility
1.4

## Slide 28: MISP ISA
Arithmetic
Data Transfer
Logical
Conditional Branch
Unconditional Jump

## Slide 29: Basic ISA
Data Transfer
Computing
Program Control
Input/Output
Processor Control
Debug
1.5

## Slide 30: Check Yourself
What MIPS instruction does this represent? Choose from one of the four options below.
1. sub $t0, $t1, $t2
2. add $t2, $t0, $t1
3. sub $t2, $t1, $t0
4. sub $t2, $t0, $t1

## Slide 31
Reading Assignment:
  Rest of P.H. Chapter 2, Appendix A
Next Lecture
  Detailed ISA and Addressing
  How does it work in MIPS?

## Slide 32: Data Transfer Instruction
Three Factors：
  Devices to store data
  Data granularities
  Addressing modes

## Slide 33: Computing Instructions
Four Factors：
  Operations: Addition, Subtraction, Multiplication, Division, etc. Comparison, Shifting, Searching, Transfer, Clear, Set, etc.
  Data representation: Fix Point, Floating Point, Logical Data, Decimal, String, Fix Point Vector, Floating Point Vector, etc.
  Data Length: Word, Half Word, Double Word, Byte, Bit, etc.
  Devices to store data：General Purpose Register, Memory, Stack, etc

## Slide 34: Program Control Instructions
Branch
Procedure Call
Return
Loop

## Slide 35: Input/Output Instructions
Usually unique direct addressing
Usually access data in byte granularity
Operations: start/stop/test/control device, data transfer
IO instructions are privileged instructions in multi-user or multi-task systems

## Slide 36: Processor Control and Debug Instructions
Two States of Processor: Supervisor Mode and User Mode--General Instructions and Privileged Instructions
Privileged Instructions:
  Set and manage the processor state
  Management of the system hardware and software
  Management of process
Debug Instructions are used to debug the hardware and software:
  Hardware Debug Instructions: Reading and Setting the key location, switch state, main registers and memory.
  Software Debug Instructions: Break point trace and trap instructions, etc