## Slide 1: Lecture7 Arithmetic-Addition/Subtraction
Computer Organization and Architecture

## Slide 2: Outline
Recap: Number Representation
Addition
Subtraction
Logical Operation
ALU

## Slide 3: Number Representation-Unsigned Binary
1.1
Given an n-bit number
Range: 0 to +2n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295
Notes: 记忆：2^32表达的十进制是10位二进制

## Slide 4: Signed Binary
1.2
Use one bit to represent the sign
+ 0.1011
+ 1100
– 1100
– 0.1011
0 1011
Position of Point
0 1100
Position of Point
1 1100
Position of Point
1 1011
Position of Point
Value Numbers in Machine
Notes: 注意定点的含义：小数点是固定的——小数在最高位，整数在最低位

## Slide 5: True Form
1.2
[x]True Form =
0，x 2n ＞ x ≥ 0
2n x 0 ≥ x ＞ 2n
Definition for Integer
x is true value n is the length
x = +1110
[x]true form = 0 , 1110
[x]true form = 24 + 1110 = 1 , 1110
x = 1110
Notes: True Form：原码

## Slide 6: True Form
1.2
Definition for Fraction
x 1 ＞ x ≥ 0
[x]true form =
1 – x 0 ≥ x ＞ 1
x = + 0.1101
[x]true form = 0 . 1101
x = 0.1101
[x]T = 1 ( 0.1101) = 1 . 1101
x = 0.1000000
[x]T = 1 ( 0.1000000) = 1 . 1000000
x = + 0.1000000
[x]T = 0 . 1000000
Notes: [x]T represents True Form of x
Fraction：分数/小数

## Slide 7: True Form
1.2
Some Problems
In some cases, addition will be implemented with subtraction!
Can we find a positive number which can substitute the negative number?
Add + +
Add
Add + -
Add - +
Add - -
Sub
Sub
Add
OP V1 V2 Real OP Sign of the Result
Positive
Positive/Negative
Positive/Negative
Negative
Notes: 提问：为何用减法代替加法？原码中可以用加法代替减法吗？

## Slide 8: Complement
1.3
Adjust the time of the clock
  The current time is 6’cloclk, but the clock is showing 9’clock. What can we do?
  Anti-clockwise: 9-3=6
  Clockwise：9+9=18, 18-12=6
  -3 can be substituted with +9, which can turn subtraction into addition.
  +9 is complement of -3 (mod 12)
The complement of a negative can be get by adding a modulo
Notes: 01101-00011=01010
01101+10011=00000
01101+11101=01010
So the conclusion should be drawn here that, the true form subtraction could be substituted with addition of complement.

## Slide 9: Complement
1.3
The complement of a negative can be get by adding a modulo.
The sum of the absolute values of a positive and negative is modulo in case of they are complements each other.
  910+310=1210，(01101)T+(10011)C=(00000)T
The complement of a positive is itself.

## Slide 10: 2’s Complement-Integer
1.3
x is the true value
n is the length
[x]C =
0，x 2n ＞ x ≥ 0
2n+1 + x 0 ＞ x ≥ 2n（mod 2n+1）
x = +1010
[x]C = 27+1 +( 1011000 )
=
[x]C = 0,1010
x = 1011000
1,0101000
1011000
100000000
Notes: 2n+1=[x]c-[x]c

## Slide 11: 2’s Complement-Fraction
1.3
x is the true value
x = + 0.1110
[x]C = 0.1110
x = 0.1100000
1.0100000
[x]C = 2 + ( 0.1100000 )
=
0.1100000
10.0000000
[x]C =
x 1 ＞ x ≥ 0
2 + x 0 ＞ x ≥ 1（mod 2）

## Slide 12: Shortcut to get complement of a negative
1.3
= 100000
= 1,0110
10101 + 1
= 1,0110
[x]T = 1,1010
[x]C = 24+1 1010
= 11111 + 1 1010
= 11111
1010
1010
+ 1
x = 1010

## Slide 13: Addition
2.0
[A]C + [B]C
= [A+B]C（mod 2n+1）
Integer
Fraction
[A]C + [B]C
= [A+B]C（mod 2）
The signs are also added together, and the generated
carry is discarded.

## Slide 14: Addition-Example
2
[A]C
[B]C
[A]C + [B]C
+
= 0 . 1 0 1 1
= 1 . 1 0 1 1
= 1 0 . 0 1 1 0
= [A + B]C
Verify
A = 0.1011，B = – 0.0101
Calculate [A + B]C
0.1011
– 0.0101
0.0110
∴ A + B = 0 . 0 1 1 0

## Slide 15: Addition-Example
2.0
[A]C
[B]C
[A]C + [B]C
+
= 1 , 0 1 1 1
= 1 , 1 0 1 1
= 1 1 , 0 0 1 0
= [A + B]C
Verify
– 1001
– 1110
– 0101
+
A = –9，B = –5
Calculate [A+B]C
∴ A + B = – 1110

## Slide 16: Subtraction
3.0
A–B
= A+(–B )
Integer
[A – B]C
= [A+(–B )]C
= [A]C + [ – B]C
(mod 2n+1)
Fraction
[A – B]C
= [A+(–B )]C
(mod 2)
= [A]C + [ – B]C

## Slide 17: Subtraction-Example
[A]C
[-B]C
[A]C + [B]C
+
= 0 , 1 0 0 1
= 1 , 1 0 1 1
= 1 0 , 0 1 0 0
= [A + B]C
Verify
1001
0100
0101
-
A = 9，B = 5
Calculate [A-B]T
∴ A - B = +0100
510 [0 , 0 1 0 1]T
-510 [1 , 1 0 1 1]C

## Slide 18: Subtraction-Example
[A]C
[-B]C
[A]C + [B]C
+
= 0 , 1 0 0 1
= 1 , 1 0 1 1
= 1 0 , 0 1 0 0
= [A + B]C
Verify
1001
0100
0101
-
A = 9，B = -5
Calculate [A+B]T
∴ A + B = +0100
-510 [1 , 1 0 1 1]C
510 [0 , 0 1 0 1]T

## Slide 19: Logic Operation
4.0
AND
OR
NOT
XOR
Bitwise operation, can be implemented with the corresponding gate.

## Slide 20: ALU- 1 bit ALU
5.0
This ALU can calculate 1-bit AND, OR and ADD operation

## Slide 21: 1-bit Full Adder
5.0
Truth Table
Input |  |  | Output |  | Notes
A | B | CarryIn | CarryOut | Sum | 
0 | 0 | 0 | 0 | 0 | 0 + 0 + 0 = 00
0 | 0 | 1 | 0 | 1 | 0 + 0 + 1 = 01
0 | 1 | 0 | 0 | 1 | 0 + 1 + 0 = 01
0 | 1 | 1 | 1 | 0 | 0 + 1 + 1 = 10
1 | 0 | 0 | 0 | 1 | 1 + 0 + 0 = 01
1 | 0 | 1 | 1 | 0 | 1 + 0 + 1 = 10
1 | 1 | 0 | 1 | 0 | 1 + 1 + 0 = 10
1 | 1 | 1 | 1 | 1 | 1 + 1 + 1 = 11

## Slide 22: CarryOut
5.0
Input |  |  | Output |  | Notes
A | B | CarryIn | CarryOut | Sum | 
0 | 0 | 0 | 0 | 0 | 0 + 0 + 0 = 00
0 | 0 | 1 | 0 | 1 | 0 + 0 + 1 = 01
0 | 1 | 0 | 0 | 1 | 0 + 1 + 0 = 01
0 | 1 | 1 | 1 | 0 | 0 + 1 + 1 = 10
1 | 0 | 0 | 0 | 1 | 1 + 0 + 0 = 01
1 | 0 | 1 | 1 | 0 | 1 + 0 + 1 = 10
1 | 1 | 0 | 1 | 0 | 1 + 1 + 0 = 10
1 | 1 | 1 | 1 | 1 | 1 + 1 + 1 = 11
CarryOut = (!A & B & CarryIn) | (A & !B & CarryIn) | (A & B & !CarryIn)| (A & B & CarryIn)
CarryOut = B & CarryIn | A & CarryIn | A & B

## Slide 23: Sum
5.0
Sum = (!A & !B & CarryIn) | (!A & B & !CarryIn) | (A & !B & !CarryIn)
| (A & B & CarryIn)
Sum= A xor B xor CarryIn
Input |  |  | Output |  | Notes
A | B | CarryIn | CarryOut | Sum | 
0 | 0 | 0 | 0 | 0 | 0 + 0 + 0 = 00
0 | 0 | 1 | 0 | 1 | 0 + 0 + 1 = 01
0 | 1 | 0 | 0 | 1 | 0 + 1 + 0 = 01
0 | 1 | 1 | 1 | 0 | 0 + 1 + 1 = 10
1 | 0 | 0 | 0 | 1 | 1 + 0 + 0 = 01
1 | 0 | 1 | 1 | 0 | 1 + 0 + 1 = 10
1 | 1 | 0 | 1 | 0 | 1 + 1 + 0 = 10
1 | 1 | 1 | 1 | 1 | 1 + 1 + 1 = 11

## Slide 24: Logic of CarryOut and Sum
5.1
CarryOut = B & CarryIn | A & CarryIn | A & B
Sum = A XOR B XOR CarryIn

## Slide 25: From 1-bit ALU to 4-bit ALU
5.2
1-bit ALU 4-bit ALU

## Slide 26: How to do subtraction?
5.3
[A+B]C=[A]C+[B]C
[A-B]C=[A]C+[-B]C
n
input：[A]C，[B]C
for subtraction：How to generate [-B]C from [B]C ?
Notes: Here by, an all-complement-inputs adder implements addition and subtraction with the Sub =1 selection in this slide.
[A]T+[B]T If A and B both positive, this equation will be the same with [A]C+[B]C, if any negative number exists, it should be considered as subtraction.
[A]T-[B]T = [A]T+[-B]T =[A]C+[B]C. Whatever the positive or negative inputs will works find with this equation.
In the second equation, if [B]T is positive, [-B]C=~[B]T+1. If [B]T is negative, as the input is [B]C and [-B]T is positive, [-B]T = [[-B]T]C = ![B]C+1.
e.g. 0100-1001=0100+0001=0101 all-complement-inputs: 0100+!(1111)+1=0100+0001=0101
The key in all-complement-inputs is to invert a complement should follow the procedure that turn it into true form, invert it, and then turn it back to complement. That means, for both positive or negative value, invert sign + complement is the equivalent with inverting bitwise plus 1.

## Slide 27: generate [-B]C from [B]C ?
5.3
[B]C=b0.b1b2…bn
If B>=0, [B]C=0.b1b2…bn=B
-B=-0.b1b2…bn
[-B]C=2+（-B）
=2-0.b1b2…bn
=1+1-0.b1b2…bn
=1+0.11…1+0.00…1-0.b1b2…bn
=1+(0.11…1-0.b1b2…bn)+0.00…1
=1+0.b1b2…bn +0.00…1
=1. b1b2…bn +0.00…1
=b0.b1b2…bn+0.00…1

## Slide 28: generate [-B]C from [B]C ?
5.3
[B]C=b0.b1b2…bn
If B<0, [B]C=1.b1b2…bn=2+B
-B=2-1.b1b2…bn
=1-0.b1b2…bn
=0.b1b2…bn+0.00…1
-B>0
[-B]C=-B
=0.b1b2…bn+0.00…1
=b0.b1b2…bn+0.00…1

## Slide 29: How to do subtraction?
5.3
[A+B]C=[A]C+[B]C
[A-B]C=[A]C+[-B]C
Invert with Sign
n
Notes: Here by, an all-complement-inputs adder implements addition and subtraction with the Sub =1 selection in this slide.
[A]T+[B]T If A and B both positive, this equation will be the same with [A]C+[B]C, if any negative number exists, it should be considered as subtraction.
[A]T-[B]T = [A]T+[-B]T =[A]C+[B]C. Whatever the positive or negative inputs will works find with this equation.
In the second equation, if [B]T is positive, [-B]C=~[B]T+1. If [B]T is negative, as the input is [B]C and [-B]T is positive, [-B]T = [[-B]T]C = ![B]C+1.
e.g. 0100-1001=0100+0001=0101 all-complement-inputs: 0100+!(1111)+1=0100+0001=0101
The key in all-complement-inputs is to invert a complement should follow the procedure that turn it into true form, invert it, and then turn it back to complement. That means, for both positive or negative value, invert sign + complement is the equivalent with inverting bitwise plus 1.

## Slide 30: Are they error?
5
7+3=10, but…
Why?
-4-5=-9, but…
Why?
Notes: In signed data type, if all bits is proceeded in arithmetic units, the overflow will effect the sign bit. That the answer of the question.

## Slide 31: Overflow
5
Overflow occurs when the result from an operation can not be represented with the available hardware.
  A 4-bit binary can represent integer from -8 to +7

## Slide 32: Overflow detection
5
Notes: 1100+1111= 11011

## Slide 33: Disadvantage of Ripple Carry Adder
5.5
The critical path is from CarryIn to CarryOut.
How can we optimize this?

## Slide 34: Fast Adder
5.5
We can reduce the delays to the carry bits by calculating them directly from the inputs, not from the outputs from the previous stage.
The trade-off is an increase in complexity for a decrease in delay.
There are two ways to produce a carry output from each stage.
  Carry Generation
  Carry Propagate

## Slide 35: Fast Adder
5.5
Carry Generation: in a given stage, a carry is generated if both a and b are 1.
 cn+1 = 1 if an = bn = 1
 | 1 | 1 |  | 
 | 1 | 0 | 1 | 1
+ | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
No carry at stage 0
Carry generated at stage 1
 gn = an bn

## Slide 36: Fast Adder
5.5
Carry Propagate: if a carry comes in to a given stage, the carry will be propagated to the next stage if either a or b is 1.
 cn+1 = 1 if cn = 1 and (an = 1 or bn = 1)
No carry
Generate
 pn = an  bn
Propagate
Note: if an = bn = cn = 1, it is
customary to count this as a
generate, but not a propagate.
Notes: For a full adder, define what happens to carries
  Generate: Cout = 1 independent of C
    G = A • B
  Propagate: Cout = C
    P = A  B
  Kill: Cout = 0 independent of C
    K = ~A • ~B
We call this logic as PGK logic

## Slide 37: Fast Adder
5.5
Note: gn and pn are already produced by the full adder circuit!!!
Adder outputs
sn = an  bn  cn = pn  cn
cn+1 = an bn + (an  bn) cn = gn + pn cn

## Slide 38: Recursion Relation with P/G Logic
5.5
To reduce delays to carry outputs, rewrite cn+1 in terms of c0, g, and p signals
  Bit 0: c1 = g0 + p0c0
  Bit 1: c2 = g1 + p1c1
  = g1 + p1g0 + p1p0c0
  Bit 2: c3 = g2 + p2c2
  = g2 + p2g1 + p2p1g0 + p2p1p0c0
  Bit 3: c4 = g3 + p3c3
  = g3 + p3g2 + p3p2g1 + p3p2p1g0 + p3p2p1p0c0
Result: Carry-lookahead adder

## Slide 39: Fast Adder
5.5
Critical paths:
  inputs to s1, s2, s3
Critical path delay = 4 gates
Drawbacks:
  Complexity, fan-ins
Comprise:
  Block CLA structure
4-Bit Carry-Look-Ahead Adder

## Slide 40: Fast Adder
5.5
When will a 4-bit adder propagate a carry from c0 to c4?
A: When it is propagated at every stage
P = p3p2p1p0
When will a 4-bit adder generate a carry output c4?
A: (1) if a carry is generated at the last stage
 OR 
(2) If it is generated at any stage and propagated through all following stages
G = g3 + p3g2 + p3p2g1 + p3p2p1g0
4-Bit Carry-Look-Ahead Adder
w/ Block Generate and Propagate

## Slide 41: Fast Adder
5.5
~G3
~P3
~G7
~G7

## Slide 42: Carry Selected Adder
8-bit Adder
  Faster
  More Cost
  3 4-bit Adders
5.5

## Slide 43: Carry Selected Adder
8-bit ALU
  Faster
  More Cost
  3 4-bit ALUs
5.5