## Slide 1: Lecture8 Arithmetic-Multiply/Division
Computer Organization and Architecture

## Slide 2: Outline
Multiplication
Division
Put them altogether: An ALU with Multiplication and Division
Notes: ALU设计目标：兼顾速度与面积！

## Slide 3: Multiplication-Steps
1.1
1000
× 1001
1000
0000
0000
1000
1001000
multiplicand
multiplier
product
Notes: 牢记这几个英文：
Multiplicand：被乘数
Multiplier：乘数
Product：乘积

## Slide 4: Multiplication-Steps
1.1
1000
× 1001
1000
0000
0000
1000
1001000
multiplicand
multiplier
product
The length of the product is considerable larger than either the multiplicand or the multiplier.

## Slide 5: Multiplication-Steps
1.1
1000
× 1001
1000
0000
0000
1000
1001000
multiplicand
multiplier
product
The length of the product is considerable larger than either the multiplicand or the multiplier.
It is much easier to implement binary multiplication
  0=>0 ( 0 X multiplicand)
  1=> multiplicand

## Slide 6: A Combinational Multiplier
1.2
For a 32-bit multiplier, how much hardware should be used? How about the critical path?
B0
A0
A1
A2
A3
A0
A1
A2
A3
A0
A1
A2
A3
A0
A1
A2
A3
B1
B2
B3
P0
P1
P2
P3
P4
P5
P6
P7
0
0
0
0

## Slide 7: How does the multiplier work?
1.2
At each level, shifts A to the left (X 2)
use next bit of B to determine whether to add in shifted multiplicand
Calculates a 2n-bit partial product at each level
B0
A0
A1
A2
A3
A0
A1
A2
A3
A0
A1
A2
A3
A0
A1
A2
A3
B1
B2
B3
P0
P1
P2
P3
P4
P5
P6
P7
0
0
0

## Slide 8: First version of the multiplication
1.3
A 64-bit register for multiplicand
A 64-bit ALU
A 64-bit register for product
A 32-bit register for multiplier
Product
Multiplier
Multiplicand
64-bit ALU
Shift Left
Shift Right
Write
Control
32 bits
64 bits
64 bits
Multiplier = datapath + control
Initially 0
Notes: 被乘数左移：以实现错位相加
乘数右移：以方便判断

## Slide 9: The First Multiplication Algorithm
1.3
Product Multiplier Multiplicand
0000 0000 0011 0000 0010
0001
0000 0100
0000 0010
0000 0010 x 0011
0000 1000
0000 0110
0000 0110
0000

## Slide 10: Inspiration of the First Multiplication
1.3
  1 clock per step=> ~ 100 clocks per multiply (3x32)
    If multiply comes as a COMMON CASE
  1/2 bits in multiplicand always 0 => 64-bit adder is wasted
  The multiplicand is shifted left 1 bit each iteration=> least significant bits of product never changed once formed
Instead of shifting multiplicand to left, shift product right?
Notes: Typically, ratio of multiply to add is 5:1 to 100:1. However if multiply comes as a common case, according to Amdahl’s law, the performance will be degraded by the increased number of multiplies.
时钟数按照2*32更加合理，因为两个移位可以并行完成。

## Slide 11: How to think of this?
1.4
B0
A0
A1
A2
A3
A0
A1
A2
A3
A0
A1
A2
A3
A0
A1
A2
A3
B1
B2
B3
P0
P1
P2
P3
P4
P5
P6
P7
0
0
0
0
Remember original combinational multiplier:
Notes: 被乘数每次左移；
乘积位置不变。

## Slide 12: Simply warp to let product move right...
1.4
Multiplicand stays still and product moves right
B0
B1
B2
B3
P0
P1
P2
P3
P4
P5
P6
P7
0
0
0
0
A0
A1
A2
A3
A0
A1
A2
A3
A0
A1
A2
A3
A0
A1
A2
A3
Notes: 与上图对比（相对运动）：
被乘数不变；
乘积每次右移；

## Slide 13: MULTIPLY HARDWARE Version 2
1.4
32-bit Multiplicand reg
32 -bit ALU
64-bit Product reg
32-bit Multiplier reg
Product
Multiplier
Multiplicand
32-bit ALU
Shift Right
Write
Control
32 bits
32 bits
64 bits
Shift Right
Notes: The product should be 65-bit register, in which MSB is for carry out, however, in this slide, it is noted as 64-bit just for comparing with the original structure.

## Slide 14: MULTIPLY HARDWARE Version 2
1.4
3. Shift the Multiplier register right 1 bit.
Done
Yes: 32 repetitions
2. Shift the Product register right 1 bit.
No: < 32 repetitions
1.
Test
Multiplier0
Multiplier0 = 0
Multiplier0 = 1
1a. Add multiplicand to the left half of product &
place the result in the left half of Product register
32nd
repetition?
Start
0000 0000 0011 0010
1: 0010 0000 0011 0010
2: 0001 0000 0011 0010
3: 0001 0000 0001 0010
1: 0011 0000 0001 0010
2: 0001 1000 0001 0010
3: 0001 1000 0000 0010
1: 0001 1000 0000 0010
2: 0000 1100 0000 0010
3: 0000 1100 0000 0010
1: 0000 1100 0000 0010
2: 0000 0110 0000 0010
3: 0000 0110 0000 0010
0000 0110 0000 0010
S: Product Multiplier Multiplicand

## Slide 15: Still more wasted space!
1.4
3. Shift the Multiplier register right 1 bit.
Done
Yes: 32 repetitions
2. Shift the Product register right 1 bit.
No: < 32 repetitions
1.
Test
Multiplier0
Multiplier0 = 0
Multiplier0 = 1
1a. Add multiplicand to the left half of product &
place the result in the left half of Product register
32nd
repetition?
Start
Product Multiplier Multiplicand
0000 0000 0011 0010
1: 0010 0000 0011 0010
2: 0001 0000 0011 0010
3: 0001 0000 0001 0010
1: 0011 0000 0001 0010
2: 0001 1000 0001 0010
3: 0001 1000 0000 0010
1: 0001 1000 0000 0010
2: 0000 1100 0000 0010
3: 0000 1100 0000 0010
1: 0000 1100 0000 0010
2: 0000 0110 0000 0010
3: 0000 0110 0000 0010
0000 0110 0000 0010
Notes: The inserted 0s waste register space. And the wasted space is just the same size with multiplier
注意蓝色部分的零都浪费了寄存器的空间。

## Slide 16: Inspiration of the Second Multiplication
1.4
Product register wastes space that exactly matches size of multiplier => combine Multiplier register and Product register
Notes: 乘积寄存器右移位数与被乘数右移位数刚好相同=>可以合并两者

## Slide 17: MULTIPLY HARDWARE Version 3
1.5
A 32-bit multiplicand reg
A 32-bit ALU
A 64-bit product reg
No specific multiplier reg (0-bit Multiplier reg)
Product
(Multiplier)
Multiplicand
32-bit ALU
Write
Control
32 bits
64 bits
Shift Right

## Slide 18: Multiply Algorithm Ver. 3
1.5
Multiplicand Product 0010 0000 0011
Done
Yes: 32 repetitions
2. Shift the Product register right 1 bit.
No: < 32 repetitions
1.
Test
Product0
Product0 = 0
Product0 = 1
1a. Add multiplicand to the left half of product &
place the result in the left half of Product register
32nd
repetition?
Start
0000 0110
.
.
.
0010
Notes: Step: Multiplicand Product
0010 0000 0011
1: 0010 0010 0011
2: 0010 0001 0001
1: 0010 0011 0001
2: 0010 0001 1000
1: 0010 0001 1000
2: 0010 0000 1100
1: 0010 0000 1100
2: 0010 0000 0110

## Slide 19: Observations on Multiply Version 3
2 steps per bit because Multiplier & Product combined
MIPS registers Hi and Lo are left and right half of Product
Gives us MIPS instruction MultU
1.5

## Slide 20: Signed Multiply
Easiest solution is to make both positive & remember whether to complement product when done (leave out the sign bit, run for 31 steps)
  Calculate the sign of the result (xor signs)
Disadvantage
  Complement is used in most machines
  Data should be converted between true value and complement multiple times
Signed multiply is implemented in complement.
1.6
Notes: In 1951，A.D Booth presented a fast multiply Algorithm in his paper “A Signed binary multiplication technique”, which is called as Booth’s Algorithm. This algorithm is aimed at the signed multiply by modifying the sign affection. If the multiplier is singed，the sign will be calculated, and if it is unsigned, a 0 extension at MSB.
早期使用原码->Booth简化了补码乘法。
安德鲁·唐纳德·布思（Andrew Donald Booth，1918年2月11日－2009年11月29日）是一位英国的工程师、物理学家与计算机科学家。他曾领导了用于计算机的磁鼓存储器的研发；此外，他还发明了布斯乘法算法。
在1943年到1945年间，布思是英国橡胶生产者研究协会（BRPRA）下辖X射线团队的一名数学物理学家。1945年后，他转职到了伦敦大学的柏贝克学院。
安德鲁·唐纳德·布思（Andrew Donald Booth，1918年2月11日－2009年11月29日）是一位英国的工程师、物理学家与计算机科学家。他曾领导了用于计算机的磁鼓存储器的研发；此外，他还发明了布斯乘法算法。
在1943年到1945年间，布思是英国橡胶生产者研究协会（BRPRA）下辖X射线团队的一名数学物理学家。1945年后，他转职到了伦敦大学的柏贝克学院。
布斯简介：布斯乘法算法是计算机中一种利用数的2的补码形式来计算乘法的算法。该算法由安德鲁·唐纳德·布斯于1950 年发明，当时他在伦敦大学伯克贝克学院做晶体学研究。布斯曾使用过台式计算器，由于用这种计算器来做移位计算比加法快，他发明了该算法来加快计算速度。布斯算法在计算机体系结构学科中备受关注。

## Slide 21: Signed Multiply-Algorithm Analysis
1.6
Multiplicand: [x]C=x0.x1x2...xn
Multiplier: [y]C=y0.y1y2...yn
[x ·y]C=？

## Slide 22: Signed Multiply-Algorithm Analysis
1.6
1）If y is positive：
[x]C=x0.x1x2...xn=2+x=2n+1+x (mod 2)
[y]C=0.y1y2...yn=y
[x]C ·[y]C=[x]C·y=（2n+1+x）·y=2n+1·y+xy
y=0.y1y2...yn=
2n+1·y=2 ， is an positive integer. (>=1)
Due to modular computation，2n+1·y=2 （mod 2）
[x]C ·[y]C=2n+1·y+xy=2+xy=[x·y]C (mod 2）
[x·y]C=[x]C ·[y]C=[x]C ·y
Notes: 在模 2 运算中，任何整数 k 乘以 2 的结果在模 2 下都是 0，即 2k≡0(mod2)

## Slide 23: Signed Multiply-Algorithm Analysis
2
2）if y is negative:
[x]C=x0.x1x2...xn
[y]C=1.y1y2...yn=2+y (mod 2)
y= [y]C-2=1.y1y2...yn-2=0.y1y2...yn-1
x·y=x(0.y1y2...yn-1)
=x(0.y1y2...yn)-x
[x·y]C=[ x(0.y1y2...yn)]C+[-x]C
0.y1y2...yn can be looked as a positive，which is similar to 1)
[ x(0.y1y2...yn)]C=[x]C(0.y1y2...yn)
[x·y]C=[x]C(0.y1y2...yn)+[-x]C
1.6

## Slide 24: Signed Multiply-Algorithm Analysis
1.6
y is positive，[x·y]C=[x]C (0.y1y2...yn)
y is negative， [x·y]C=[x]C(0.y1y2...yn)+[-x]C
y0=0 when y is positive, otherwise y0=1
So we have：
y is positive， [x·y]C=[x]C (0.y1y2...yn)+[-x]C ·y0
y is negative， [x·y]C=[x]C (0.y1y2...yn)+[-x]C ·y0
In summary：[x·y]C=[x]C (0.y1y2...yn)+[-x]C ·y0
We can prove ：[-x]C =-[x]C
Conclusion ：[x·y]C=[x]C(0.y1y2...yn)-[x]C ·y0

## Slide 25: Booth’s Multiplication Algorithm
1.7
Take 2’s complement fraction for example
[x]C = x0. x1x2 xn
…
[y]C = y0. y1y2 yn
…
If y is positive, y0=0. Can be calculated in the same way of unsigned multiplication. The sign can be generated naturally
If y is negative, y0=1. Can be calculated in the same way of unsigned multiplication while not consider y0 . Finally adjust the product by adding [–x]C.
Notes: For a negative integer multiplier:
[y]C= 2n+1+[y]T[y]C-[y}T=

## Slide 26: Booth’s Multiplication Algorithm
1.7
[x · y]C
= [x]C( 0.y1 yn ) – [x]C · y0
…
= [x]C(y1 2-1+y22-2+ +yn2-n) – [x]C · y0
…
= [x]C(–y0+y1 2-1+y22-2+ +yn2-n)
…
= [x]C[–y0+(y1 – y12-1)+(y22-1–y22-2)+ +(yn2-(n-1)–yn2-n)]
…
= [x]C[(y1–y0)+(y2–y1)2-1+ +(yn–yn-1)2-(n-1)+(0 –yn)2-n)]
…
–[x]C= +[–x]C
2-1 = 20 – 2-1
2-2 = 2-1 – 2-2
= [x]C[(y1–y0)+(y2–y1)2-1+ +(yn+1–yn)2-n]
…
additional bit yn+1
[x]C = x0.x1x2 xn [y]C = y0.y1y2 yn
…
…
Notes: It is noted that, as the complement has change the value of number by modulo 2, it is not describe the value directly, and can not be modified the sign directly to present a negative number.
Also this slide is for negative multiply.
[0010]T*[1011]T=[1110]T
[0010]C*[1101]C=[0010]C*[0101]-[0010]C*1=

## Slide 27: Booth’s Multiplication Algorithm
1.7
[z0]C= 0
[z1]C= 2-1{(yn+1–yn)[x]C+[z0]C} yn+1 = 0
[zn]C= 2-1{(y2–y1)[x]C+[zn-1]C}
…
[x · y]C= [zn]C+(y1–y0)[x]C
It does not shift at the last step!
How to implement
yi+1–yi ?
0 0
0 1
1 0
1 1
1
+[x]C 1
+[–x]C 1
1
0
1
-1
0
yi yi+1
OP
yi+1–yi

## Slide 28: Booth’s Algorithm
Current Bit Bit to the Right Explanation Example Op
1 0 Begins run of 1s 0001111000 sub & shr
1 1 Middle of run of 1s 0001111000 shr
0 1 End of run of 1s 0001111000 add & shr
0 0 Middle of run of 0s 0001111000 shr
Originally for Speed (when shift was faster than add)
Replace a string of 1s in multiplier with an initial subtract when we first see a one and then later add for the bit after the last one
0 1 1 1 1 0
beginning of run
end of run
middle of run
–1
+ 10000
01111
Notes: 这里可以看到一个booth乘法的直观解释，也便于booth乘法步骤的记忆。
类似×00001，肯定是要加被乘数；
类似*01111等价于 *（10000-1），因此要减去被乘数再移位。
参考资料：https://baike.baidu.com/item/%E5%B8%83%E6%96%AF%E4%B9%98%E6%B3%95%E7%AE%97%E6%B3%95

## Slide 29: Examples for Booth’s Algorithm
1.7
2 X 7
1a. P = P - m 1110 + 1110 1110 0111 0 shift P (sign ext)
1b. 0010 1111 0011 1 11 -> nop, shift
2. 0010 1111 1001 1 11 -> nop, shift
3. 0010 1111 1100 1 01 -> add
4a. 0010 + 0010
0001 1100 1 shift
4b. 0010 0000 1110 0 done
Operation Multiplicand Product next?
0. initial value 0010 0000 0111 0 10 -> sub
Notes: 注意乘积右移时最高位要补符号位：算术右移！

## Slide 30: Examples for Booth’s Algorithm
1.7
2 X (-3)
Operation Multiplicand Product next?
0. initial value 0010 0000 1101 0 10 -> sub
1a. P = P - m 1110 +1110 1110 1101 0 shift P (sign ext)
1b. 0010 1111 0110 1 01 -> add + 0010
2a. 0001 0110 1 shift P
2b. 0010 0000 1011 0 10 -> sub +1110
3a. 0010 1110 1011 0 shift
3b. 0010 1111 0101 1 11 -> nop
4a 1111 0101 1 shift
4b. 0010 1111 1010 1 done
Notes: 在线计算器：
http://www.ecs.umass.edu/ece/koren/arith/simulator/Booth/

## Slide 31: Implementation of Booth’s Multiplication
1.7
Some details are missed

## Slide 32: Implementation of Booth’s Multiplication
1.7

## Slide 33: Calculate Division Manually
2.1
1001
1000 1001010
-1000
10
101
1010
-1000
10
quotient
dividend
remainder
divisor
n-bit operands yield n-bit quotient and remainder
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit

## Slide 34: How to calculate division automatically?
2.2
Do the subtract first
If remainder >=0, the corresponding quotient bit is 1
if remainder goes < 0, the corresponding quotient shift left, add divisor back

## Slide 35: First version of division hardware
2.3
A 64-bit register for divisor
A 64-bit ALU
A 64-bit register for remainder
A 32-bit register for quotient
Remainder
Quotient
Divisor
64-bit ALU
Shift Right
Shift Left
Write
Control
32 bits
64 bits
64 bits

## Slide 36: An example-7/2
2.3

## Slide 37: Division Algorithm
2.3
2b. Restore the original value by adding the
Divisor register to the Remainder register, &
place the sum in the Remainder register. Also
shift the Quotient register to the left, setting
the new least significant bit to 0.
Takes n+1 steps for n-bit Quotient & Rem.
Remainder Quotient Divisor 0000 0111 0000 0010 0000
Test Remainder
Remainder < 0
Remainder  0
1. Subtract the Divisor register from the
Remainder register, and place the result
in the Remainder register.
2a. Shift the
Quotient register
to the left setting
the new rightmost
bit to 1.
3. Shift the Divisor register right1 bit.
Done
Yes: n+1 repetitions (n = 4 here)
Start: Place Dividend in Remainder
n+1
repetition?
No: < n+1 repetitions

## Slide 38: Inspiration of the First Division
2.3
  Half of the 64-bit divisor is always 0.
  Half of 64-bit adder is wasted.
  Half of the divisor is wasted.
Can the right shifting of the divisor be substituted by the left shifting of the reminder?

## Slide 39: The second Division
2.4
A 32-bit register for divisor
A 32-bit ALU
A 64-bit register for remainder
A 32-bit register for quotient
Remainder
Quotient
Divisor
32-bit ALU
Shift Left
Write
Control
32 bits
32 bits
64 bits
Shift Left

## Slide 40: Divide Algorithm V2
2.4
Remainder Quotient Divisor 0000 0111 0000 0010
3b. Restore the original value by adding the Divisor
register to the left half of the Remainderregister,
&place the sum in the left half of the Remainder
register. Also shift the Quotient register to the left,
setting the new least significant bit to 0.
Test Remainder
Remainder < 0
Remainder  0
2. Subtract the Divisor register from the left half of the Remainder register, & place the
result in the left half of the Remainder register.
3a. Shift the
Quotient register
to the left setting
the new rightmost
bit to 1.
1. Shift the Remainder register left 1 bit.
Done
Yes: n repetitions (n = 4 here)
nth
repetition?
No: < n repetitions
Start: Place Dividend in Remainder

## Slide 41: An example 7/2
2.4

## Slide 42: Inspiration of the Second Division
Quotient register wastes space that exactly matches size of remainder => combine Remainder register and Quotient register by shifting quotient reg left
  Beginning with shifting remainder
  However a redundant shift happens as in a loop
  Left half should be shift back at the end
2.4

## Slide 43: The third division
2.5
A 32-bit register for divisor
A 32-bit ALU
A 64-bit register for remainder
No specific register for quotient (0-bit)
Remainder
(Quotient)
Divisor
32-bit ALU
Write
Control
32 bits
64 bits
Shift Left
“HI”
“LO”

## Slide 44: Divide Algorithm V3
2.5
Remainder Divisor 0000 0111 0010
3b. Restore the original value by adding the Divisor
register to the left half of the Remainder register,
&place the sum in the left half of the Remainder
register. Also shift the Remainder register to the
left, setting the new least significant bit to 0.
Test Remainder
Remainder < 0
Remainder  0
2. Subtract the Divisor register from the left half of the Remainder register, & place the
result in the left half of the Remainder register.
3a. Shift the
Remainder register
to the left setting
the new rightmost
bit to 1.
1. Shift the Remainder register left 1 bit.
Done. Shift left half of Remainder right 1 bit.
Yes: n repetitions (n = 4 here)
nth
repetition?
No: < n repetitions
Start: Place Dividend in Remainder

## Slide 45: An example
2.5

## Slide 46: Inspiration of the third division
2.5
The hardware of multiplication and division are identical.
  A ALU to perform addition or subtraction
  A 64-bit register which can be shifted to left or right.
Hi and Lo registers in MIPS can be merged together as 64-bit register for multiplication and division.
Signed division
  The sign is calculated separately.
  Perform unsigned division
  Adjust the quotient and the remainder
  The remainder must has the same sign with the dividend
  Also has fast algorithm in complement form

## Slide 47: An ALU with Multiplication and Division
3

## Slide 48: Adder

## Slide 49: MULTIPLY HARDWARE Version 3
1.5
A 32-bit multiplicand reg
A 32-bit ALU
A 64-bit product reg
No specific multiplier reg (0-bit Multiplier reg)
Product
(Multiplier)
Multiplicand
32-bit ALU
Write
Control
32 bits
64 bits
Shift Right

## Slide 50: The third division
2.5
A 32-bit register for divisor
A 32-bit ALU
A 64-bit register for remainder
No specific register for quotient (0-bit)
Remainder
(Quotient)
Divisor
32-bit ALU
Write
Control
32 bits
64 bits
Shift Left
“HI”
“LO”