## Slide 1: Lecture10 Single Cycle CPU - DataPath
Computer Organization and Architecture

## Slide 2: Outline
Introduction
How to design a microprocessor
Datapath for R-R operation and its timing
Datapath for logical operation with imm.
Datapath for load and store operation
Datapath for branch and jump operation
Put it together: A single cycle datapath

## Slide 3: Where are we now?
1.1
The Five Classic Components of a Computer
Lecture10’s Goal: Design a Single Cycle Processor
Control
Datapath
Memory
Processor
Input
Output

## Slide 4: The Performance Perspective
1.2
Performance of a machine is determined by:
  Instruction count
  Clock cycle time
  Clock cycles per instruction
Processor design (datapath and control) will determine:
  Clock cycle time
  Clock cycles per instruction
Today:Single cycle processor:
  Advantage: One clock cycle per instruction
  Disadvantage: long cycle time
CPI
Inst. Count
Cycle Time

## Slide 5: How to Design a Processor: step-by-step
2
1. Analyze instruction set => datapath requirements
  the meaning of each instruction is given by the register transfers
  datapath must include storage element for ISA registers
    possibly more
  datapath must support each register transfer
2. Select set of datapath components and establish clocking methodology
3. Assemble datapath meeting the requirements
4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
5. Assemble the control logic

## Slide 6: The MIPS Instruction Formats
2.1
All MIPS instructions are 32 bits long. The three instruction formats:
  R-type
  I-type
  J-type
The different fields are:
  op: operation of the instruction
  rs, rt, rd: the source and destination register specifiers
  shamt: shift amount
  funct: selects the variant of the operation in the “op” field
  address / immediate: address offset or immediate value
  target address: target address of the jump instruction
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 7: Step 1a: The MIPS-lite Subset for today
2.2
ADD and SUB
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE Word
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 8: Logical Register Transfers
2.3
RTL gives the meaning of the instructions
All start by fetching the instruction
op | rs | rt | rd | shamt | funct = MEM[ PC ]
op | rs | rt | Imm16 = MEM[ PC ]
inst Register Transfers
ADD R[rd] <– R[rs] + R[rt]; PC <– PC + 4
SUB R[rd] <– R[rs] – R[rt]; PC <– PC + 4
ORi R[rt] <– R[rs] | zero_ext(Imm16); PC <– PC + 4
LOAD R[rt] <– MEM[ R[rs] + sign_ext(Imm16)]; PC <– PC + 4
STORE MEM[ R[rs] + sign_ext(Imm16) ] <– R[rt]; PC <– PC + 4
BEQ if ( R[rs] == R[rt] ) then
PC <– PC + 4 + sign_ext(Imm16)] || 00
else
PC <– PC + 4
Notes: 1) In Beq instruction, if ALU determines the equations, a better implementation will be a subtraction and with a zero output for branch.
2) || means add two bits at the end of immediate address bias, which is transfer the word address into byte address (4 bytes in 1 word). This is a quit useful design for MIPS PC-relative and PC direct addressing. That also means the an 18 bits immediate address displacement and a 28 bits instruction jumps address.

## Slide 9: Step 1: Requirements of ISA
2.4
Memory
  instruction & data
Registers (32 x 32)
  read RS
  read RT
  Write RT or RD
PC
Extender
Add and Sub register or extended immediate
Add 4 or extended immediate to PC

## Slide 10: Step 2: Components of the Datapath
2.5
Combinational Elements
Storage Elements
  Clocking methodology

## Slide 11: Combinational Logic Elements (Basic Building Blocks)
2.6
x = 1011000
Adder
MUX
ALU

## Slide 12: Storage Element: Register (Basic Building Block)
2.7
Register
  Similar to the D Flip Flop except
    N-bit input and output
    Write Enable input
  Write Enable:
    negated (0): Data Out will not change
    asserted (1): Data Out will become Data In
Clk
Data In
Write Enable
N
N
Data Out

## Slide 13: Storage Element: Register File
2.8
Register File consists of 32 registers:
  Two 32-bit output busses:
  busA and busB
  One 32-bit input bus: busW
Register is selected by:
  RA (number) selects the register to put on busA (data)
  RB (number) selects the register to put on busB (data)
  RW (number) selects the register to be written via busW (data) when Write Enable is 1
Clock input (CLK)
  The CLK input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block:
    RA or RB valid => busA or busB valid after “access time.”
Clk
busW
Write Enable
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 32-bit
Registers
Notes: Although we said the clock only is a factor for write operation, the read processing still needs sequential control in case the conflict happens between write and read.

## Slide 14: Storage Element: Idealized Memory
2.9
Memory (idealized)
  One input bus: Data In
  One output bus: Data Out
Memory word is selected by:
  Address selects the word to put on Data Out
  Write Enable = 1: address selects the memory word to be written via the Data In bus
Clock input (CLK)
  The CLK input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block:
    Address valid => Data Out valid after “access time.”
Clk
Data In
Write Enable
32
32
DataOut
Address
Notes: Although we said the clock only is a factor for write operation, the read processing still needs sequential control in case the conflict happens between write and read.

## Slide 15: Clocking Methodology
2.10
All storage elements are clocked by the same clock edge
Cycle Time = CLK-to-Q + Longest Delay Path + Setup + Clock Skew
(CLK-to-Q + Shortest Delay Path - Clock Skew) > Hold Time
Clk
Don’t Care
Setup
Hold
.
.
.
.
.
.
.
.
.
.
.
.
Setup
Hold
Notes: Max delay and Min delay

## Slide 16: 3a: Overview of the Instruction Fetch Unit
3
The common RTL operations
  Fetch the Instruction: mem[PC]
  Update the program counter:
    Sequential Code: PC <- PC + 4
    Branch and Jump: PC <- “something else”
32
Instruction Word
Address
Instruction
Memory
PC
Clk
Next Address
Logic

## Slide 17: 3b: Add & Subtract
3.1
R[rd] <- R[rs] op R[rt] Example: addU rd, rs, rt
  Ra, Rb, and Rw come from instruction’s rs, rt, and rd fields
  ALUctr and RegWr: control logic after decoding the instruction
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
32
Result
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rd
ALU

## Slide 18: Register-Register Timing: One complete cycle
3.2
Clk
PC
Rs, Rt, Rd,
Op, Func
Clk-to-Q
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA, B
Register File Access Time
Old Value
New Value
busW
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
Register Write
Occurs Here
32
Result
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rd
ALU

## Slide 19: 3c: Logical Operations with Immediate
4
R[rt] <- R[rs] op ZeroExt[imm16] ]
11
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
rd?
immediate
0
16
15
31
16 bits
16 bits
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
32
Result
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
ZeroExt
Mux
Rt
Rd
RegDst
Mux
32
16
imm16
ALUSrc
ALU
Rt?

## Slide 20: 3d: Load Operations
R[rt] <- Mem[R[rs] + SignExt[imm16]] Example: lw rt, rs, imm16
11
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
rd
5.1
32
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rd
RegDst
Extender
Mux
Mux
32
16
imm16
ALUSrc
ExtOp
Clk
Data In
WrEn
32
Adr
Data
Memory
32
ALU
MemWr
Mux
W_Src
??
Rt?

## Slide 21: 3e: Store Operations
Mem[ R[rs] + SignExt[imm16] <- R[rt] ] Example: sw rt, rs, imm16
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
5.2
32
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst
Extender
Mux
Mux
32
16
imm16
ALUSrc
ExtOp
Clk
Data In
WrEn
32
Adr
Data
Memory
MemWr
ALU
32
Mux
W_Src

## Slide 22: 3f: The Branch Instruction
6.1
beq rs, rt, imm16
  mem[PC] Fetch the instruction from memory
  Equal <- R[rs] == R[rt] Calculate the branch condition
  if (Equal) Calculate the next instruction’s address
    PC <- PC + 4 + ( SignExt(imm16) x 4 )
  else
    PC <- PC + 4
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 23: Datapath for Branch Operations
6.1
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst
Extender
Mux
Mux
32
16
imm16
ALUSrc
ExtOp
ALU
32
Instruction Word
Address
Instruction
Memory
PC
Clk
Next Address
Logic
ZERO
Branch
beq rs, rt, imm16 Datapath generates condition (equal)
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 24: Calculate the address of the next ins
6.2

## Slide 25: Calculate the address of the next Inst
PC stores a byte accessing address with 32-bit width
  Next Inst Accessing: PC<31:0>=PC<31:0>+4
  PC-relative Accessing: PC<31:0>=PC<31:0>+4+SignExt[Imm16]x4
Odd address? Why
  32bit PC
  4 bytes Instruction
AKA.
  2 LSB (Least two Significant) bits of 32-bit PC are 00 !Lol
  No more storage space for these 2 bits
Practically, only 30-bit PC<31:2> in typical hardware
  Next Inst Accessing: PC<31:2>=PC<31:2>+1 (1 word)
  PC-relative Accessing :PC<31:2>=PC<31:2>+1+SignExt[Imm16]
  Other: Inst mem address = PC<31:2>||00
6.2
Notes: || means adding 2 zero at LSB of 30-bit PC.

## Slide 26: Logic for next address calculating: an expensive but fast method
30-bit PC:
  Sequential operation: PC<31:2>=PC<31:2>+1
  Branch operation: PC<31:2>=PC<31:2>+1+SignExt[Imm16]
  Others: Address to access ins-memory=PC<31:2>||00
6.3

## Slide 27: Logic for next address calculating: an cheap but slow method
Why slow?
The adder cannot begin to calculate the address until the 'Zero'(ALU) is generated!
Can this method hurt the performance?
In this design, the answer is NO, as load operation is the critical path.
6.3

## Slide 28: Datapath for Branch Operations
6.4
beq rs, rt, imm16 Datapath generates condition (equal)
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
32
imm16
PC
Clk
00
Adder
Mux
Adder
4
nPC_sel
Clk
busW
RegWr
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Equal?
Cond
PC Ext
Inst Address

## Slide 29: jump operation
6.5
op
target address
0
26
31
6 bits
26 bits
j target
mem[PC]
PC<31:2>=PC<31:28>||target<25:0>

## Slide 30: Instruction Fetch Unit
6.5

## Slide 31: Putting it All Together: A Single Cycle Datapath(Except Jump Operation)
7
imm16
32
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst
Extender
Mux
32
16
imm16
ALUSrc
ExtOp
Mux
MemtoReg
Clk
Data In
WrEn
32
Adr
Data
Memory
MemWr
ALU
Equal
Instruction<31:0>
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
=
Adder
Adder
PC
Clk
00
Mux
4
nPC_sel
PC Ext
Adr
Inst
Memory

## Slide 32: step4:determine setting of control points
7.1

## Slide 33: A Real MIPS Chip Datapath
7.2
Notes: T0 was developed as part of the CNS-1 project in a collaboration between researchers in the Computer Science Division of the University of California at Berkeley and the Realization Group at the International Computer Science Institute.
T0 (Torrent-0) is a single-chip fixed-point vector microprocessor designed for multimedia, human-interface, neural network, and other digital signal processing tasks. T0 includes a MIPS-II compatible 32-bit integer RISC core, a 1KB instruction cache, a high performance fixed-point vector coprocessor, a 128-bit wide external memory interface, and a byte-serial host interface.

## Slide 34: T0 Vector Microprocessor (1995)
Lane
Vector register elements striped over lanes
[0]
[8]
[16]
[24]
[1]
[9]
[17]
[25]
[2]
[10]
[18]
[26]
[3]
[11]
[19]
[27]
[4]
[12]
[20]
[28]
[5]
[13]
[21]
[29]
[6]
[14]
[22]
[30]
[7]
[15]
[23]
[31]
Notes: T0 was developed as part of the CNS-1 project in a collaboration between researchers in the Computer Science Division of the University of California at Berkeley and the Realization Group at the International Computer Science Institute.
T0 (Torrent-0) is a single-chip fixed-point vector microprocessor designed for multimedia, human-interface, neural network, and other digital signal processing tasks. T0 includes a MIPS-II compatible 32-bit integer RISC core, a 1KB instruction cache, a high performance fixed-point vector coprocessor, a 128-bit wide external memory interface, and a byte-serial host interface.

## Slide 35: Check Your Self
Which of the following is correct for a load instruction? Refer to Figure 4.10.
  MemtoReg should be set to cause the data from memory to be sent to the register file.
  MemtoReg should be set to cause the correct register destination to be sent to the register file.
  We do not care about the setting of MemtoReg for loads.
Notes: Answer: a

## Slide 36: Check Your Self
The single-cycle datapath conceptually described in this section must have separate instruction and data memories, because
  the formats of data and instructions are different in MIPS, and hence different memories are needed.
  having separate memories is less expensive.
  the processor operates in one cycle and cannot use a single-ported memory for two different accesses within that cycle
Notes: Answer: c

## Slide 37: Next Time
How to generate the control signals for single cycle datapath.
8