## Slide 1: Lecture11 Single Cycle CPU – Control Path
Computer Organization and Architecture

## Slide 2: Outline
Recap design steps (5 steps)
Recap Single Cycle Data Path and analyze Control Signals
Implementations
Evaluation and Analyzing
Summary

## Slide 3: Where are we now?
1.1
The Five Classic Components of a Computer
Today's Topic: Design a Single Cycle Processor
Control
Datapath
Memory
Processor
Input
Output

## Slide 4: Recap: Summary from last time
1.2
5 steps to design a processor
  1. Analyze instruction set => datapath requirements
  2. Select set of datapath components & establish clock methodology
  3. Assemble datapath meeting the requirements
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
  5. Assemble the control logic
MIPS makes it easier
  Instructions same size
  Source registers always in same place
  Immediates same size, location
  Operations always on registers/immediates
Single cycle datapath  CPI=1, Cycle Time = long!

## Slide 5: Recap: The MIPS Instruction Formats
2.1
All MIPS instructions are 32 bits long. The three instruction formats:
  R-type
  I-type
  J-type
The different fields are:
  op: operation of the instruction
  rs, rt, rd: the source and destination register specifiers
  shamt: shift amount
  funct: selects the variant of the operation in the “op” field
  address / immediate: address offset or immediate value
  target address: target address of the jump instruction
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 6: Recap: The MIPS Instruction Formats
2.1
All MIPS instructions are 32 bits long. The three instruction formats:
  R-type
  I-type
  J-type
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 7: An Abstract View of the Implementation
2.2
Data
Out
Clk
5
Rw
Ra
Rb
32 32-bit
Registers
Rd
ALU
Clk
Data In
Data
Address
Ideal
Data
Memory
Instruction
Instruction
Address
Ideal
Instruction
Memory
Clk
PC
5
Rs
5
Rt
32
32
32
32
A
B
Next Address
Control
Datapath
Control Signals
Conditions

## Slide 8: Recap: A Single Cycle Datapath
2.3
Rs, Rt, Rd and Imed16 hardwired into datapath from Fetch Unit
We have everything except control signals (underline)
  Today’s lecture will show you how to generate the control signals

## Slide 9: Recap: Meaning of the Control Signals
2.4
nPC_MUX_sel: 0  PC <– PC + 4 1  PC <– PC + 4 + SignExt(Im16) || 00
Later in lecture: higher-level connection between mux and branch cond
Adr
Inst
Memory
Adder
Adder
PC
Clk
00
Mux
4
nPC_MUX_sel
PC Ext
imm16

## Slide 10: Recap: Meaning of the Control Signals
2.5
ExtOp: “zero”, “sign”
ALUsrc: 0  regB; 1  immed
ALUctr: “add”, “sub”, “or”
MemWr: 1  write memory
MemtoReg: 0  ALU; 1  Mem
RegDst: 0  “rt”; 1  “rd”
RegWr: 1  write register

## Slide 11: RTL: The Add Instruction
2.6
x = 1011000
add rd, rs, rt
  mem[PC] Fetch the instruction from memory
  R[rd] <- R[rs] + R[rt] The actual operation
  PC <- PC + 4 Calculate the next instruction’s address
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 12: Instruction Fetch Unit at the Beginning of Add
2.7
Fetch the instruction from Instruction memory: Instruction <- mem[PC]
  This is the same for all instructions
PC Ext
Adr
Inst
Memory
Adder
Adder
PC
Clk
00
Mux
4
nPC_MUX_sel
imm16
Instruction<31:0>

## Slide 13: The Single Cycle Datapath during Add
2.8
R[rd] <- R[rs] + R[rt]
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31

## Slide 14: Instruction Fetch Unit at the End of Add
2.9
PC <- PC + 4
  This is the same for all instructions except: Branch and Jump
Instruction Fetch Unit at the End of Add
Adr
Inst
Memory
Adder
Adder
PC
Clk
00
Mux
4
nPC_MUX_sel
imm16
Instruction<31:0>
0
1

## Slide 15: The Single Cycle Datapath during Or Immediate
2.10
R[rt] <- R[rs] or ZeroExt[Imm16]
op
rs
rt
immediate
0
16
21
26
31

## Slide 16: The Single Cycle Datapath during Or Immediate
3
R[rt] <- R[rs] or ZeroExt[Imm16]
op
rs
rt
immediate
0
16
21
26
31

## Slide 17: The Single Cycle Datapath during Load
3.1
R[rt] <- Data Memory {R[rs] + SignExt[imm16]}
op
rs
rt
immediate
0
16
21
26
31

## Slide 18: The Single Cycle Datapath during Store
3.2
Data Memory {R[rs] + SignExt[imm16]} <- R[rt]
op
rs
rt
immediate
0
16
21
26
31

## Slide 19: The Single Cycle Datapath during Store
3.2
Data Memory {R[rs] + SignExt[imm16]} <- R[rt]
op
rs
rt
immediate
0
16
21
26
31

## Slide 20: The Single Cycle Datapath during Branch
4
if (R[rs] - R[rt] == 0) then Zero <- 1 ; else Zero <- 0
op
rs
rt
immediate
0
16
21
26
31

## Slide 21: Instruction Fetch Unit at the End of Branch
5.1
if (Zero == 1) then PC = PC + 4 + SignExt[imm16]*4 ; else PC = PC + 4
op
rs
rt
immediate
0
16
21
26
31
What is encoding of nPC_sel?
  Direct MUX select?
  Branch / not branch
Let’s choose second option
Adr
Inst
Memory
Adder
Adder
PC
Clk
00
Mux
4
nPC_sel
imm16
Instruction<31:0>
0
1
Zero
nPC_MUX_sel

## Slide 22: Step 4: Given Datapath: RTL -> Control
5.2

## Slide 23: A Summary of Control Signals
6.1
inst Register Transfer
ADD R[rd] <– R[rs] + R[rt]; PC <– PC + 4
ALUsrc = RegB, ALUctr = “add”, RegDst = rd, RegWr, nPC_sel = “+4”
SUB R[rd] <– R[rs] – R[rt]; PC <– PC + 4
ALUsrc = RegB, ALUctr = “sub”, RegDst = rd, RegWr, nPC_sel = “+4”
ORi R[rt] <– R[rs] + zero_ext(Imm16); PC <– PC + 4
ALUsrc = Im, Extop = “Z”, ALUctr = “or”, RegDst = rt, RegWr, nPC_sel = “+4”
LOAD R[rt] <– MEM[ R[rs] + sign_ext(Imm16)]; PC <– PC + 4
ALUsrc = Im, Extop = “Sn”, ALUctr = “add”, MemtoReg, RegDst = rt, RegWr, nPC_sel = “+4”
STORE MEM[ R[rs] + sign_ext(Imm16)] <– R[rs]; PC <– PC + 4
ALUsrc = Im, Extop = “Sn”, ALUctr = “add”, MemWr, nPC_sel = “+4”
BEQ if ( R[rs] == R[rt] ) then PC <– PC + sign_ext(Imm16)] || 00 else PC <– PC + 4
nPC_sel = “Br”, ALUctr = “sub”
SLT if R[rs]< R[rt] then R[rd] = 1 PC <– PC + 4 else R[rd] = [0] PC <– PC + 4
ALUsrc=RegB, ALUctr=“slt”, RegDst=rd, RegWr, nPC_sel=“+4”

## Slide 24: A Summary of the Control Signals
6.1
add
sub
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPCsel
Jump
ExtOp
ALUop<N:0>
1
0
0
1
0
0
0
x
Add
1
0
0
1
0
0
0
x
Subtract
0
1
0
1
0
0
0
0
Or
0
1
1
1
0
0
0
1
Add
x
1
x
0
1
0
0
1
Add
x
0
x
0
0
1
0
x
Subtract
x
x
x
0
0
0
1
x
xxx
op
target address
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
op
rs
rt
immediate
R-type
I-type
J-type
add, sub
ori, lw, sw, beq
jump
func
op
00 0000
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
Appendix A
10 0000
See
10 0010
We Don’t Care :-)
10 1010
00 0000
slt
Same to sub

## Slide 25: The Concept of Local Decoding
6.2
R-type
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
Branch
Jump
ExtOp
ALUop<N:0>
1
0
0
1
0
0
0
x
“R-type”
0
1
0
1
0
0
0
0
Or
0
1
1
1
0
0
0
1
Add
x
1
x
0
1
0
0
1
Add
x
0
x
0
0
1
0
x
Subtract
x
x
x
0
0
0
1
x
xxx
op
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010

## Slide 26: The Encoding of ALUop
6.3
Main
Control
op
6
ALU
Control
(Local)
func
N
6
ALUop
ALUctr
3
R-type
ori
lw
sw
beq
jump
ALUop (Symbolic)
“R-type”
Or
Add
Add
Subtract
xxx
ALUop<2:0>
1 00
0 10
0 00
0 00
0 01
xxx
In this exercise, ALUop has to be 2 bits wide to represent:
  (1) “R-type” instructions
  “I-type” instructions that require the ALU to perform:
    (2) Or, (3) Add, and (4) Subtract
To implement the full MIPS ISA, ALUop has to be 3 bits to represent:
  (1) “R-type” instructions
  “I-type” instructions that require the ALU to perform:
    (2) Or, (3) Add, (4) Subtract, and (5) And (Example: andi)

## Slide 27: The Decoding of the “func” Field
6.3
R-type
ori
lw
sw
beq
jump
ALUop (Symbolic)
“R-type”
Or
Add
Add
Subtract
xxx
ALUop<2:0>
1 00
0 10
0 00
0 00
0 01
xxx
Main
Control
op
6
ALU
Control
(Local)
func
N
6
ALUop
ALUctr
3
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
R-type
funct<5:0>
Instruction Operation
10 0000
10 0010
10 0100
10 0101
10 1010
add
subtract
and
or
set-on-less-than
ALUctr<2:0>
ALU Operation
000
001
010
110
111
And
Or
Add
Subtract
Set-on-less-than
P. 286 text:
ALUctr
ALU

## Slide 28: The Truth Table for ALUctr
6.4
R-type
ori
lw
sw
beq
ALUop
(Symbolic)
“R-type”
Or
Add
Add
Subtract
ALUop<2:0>
1 00
0 10
0 00
0 00
0 01
ALUop
func
bit<2>
bit<1>
bit<0>
bit<2>
bit<1>
bit<0>
bit<3>
0
0
0
x
x
x
x
ALUctr
ALU
Operation
Add
0
1
0
bit<2>
bit<1>
bit<0>
0
x
1
x
x
x
x
Subtract
1
1
0
0
1
x
x
x
x
x
Or
0
0
1
1
x
x
0
0
0
0
Add
0
1
0
1
x
x
0
0
1
0
Subtract
1
1
0
1
x
x
0
1
0
0
And
0
0
0
1
x
x
0
1
0
1
Or
0
0
1
1
x
x
1
0
1
0
Set on <
1
1
1
funct<3:0>
Instruction Op.
0000
0010
0100
0101
1010
add
subtract
and
or
set-on-less-than

## Slide 29: The Logic Equation for ALUctr<2>
6.5
ALUop
func
bit<2>
bit<1>
bit<0>
bit<2>
bit<1>
bit<0>
bit<3>
ALUctr<2>
0
x
1
x
x
x
x
1
1
x
x
0
0
1
0
1
1
x
x
1
0
1
0
1
ALUctr<2> = !ALUop<2> & ALUop<0> +
  ALUop<2> & !func<2> & func<1> & !func<0>
This makes func<3> a don’t care

## Slide 30: The Logic Equation for ALUctr<1>
6.5
ALUop
func
bit<2>
bit<1>
bit<0>
bit<2>
bit<1>
bit<0>
bit<3>
0
0
0
x
x
x
x
1
ALUctr<1>
0
x
1
x
x
x
x
1
1
x
x
0
0
0
0
1
1
x
x
0
0
1
0
1
1
x
x
1
0
1
0
1
ALUctr<1> = !ALUop<2> & !ALUop<1> +
  ALUop<2> & !func<2> & !func<0>

## Slide 31: The Logic Equation for ALUctr<0>
7
ALUop
func
bit<2>
bit<1>
bit<0>
bit<2>
bit<1>
bit<0>
bit<3>
ALUctr<0>
0
1
x
x
x
x
x
1
1
x
x
0
1
0
1
1
1
x
x
1
0
1
0
1
ALUctr<0> = !ALUop<2> & ALUop<1>
  + ALUop<2> & !func<3> & func<2> & !func<1> & func<0>
  + ALUop<2> & func<3> & !func<2> & func<1> & !func<0>

## Slide 32: The ALU Control Block
7.1
ALU
Control
(Local)
func
3
6
ALUop
ALUctr
3
ALUctr<2> = !ALUop<2> & ALUop<0> +
  ALUop<2> & !func<2> & func<1> & !func<0>
ALUctr<1> = !ALUop<2> & !ALUop<1> + !ALUop<2> +
  ALUop<2> & !func<2> & !func<0>
ALUctr<0> = !ALUop<2> & ALUop<1>
  + ALUop<2> & !func<3> & func<2> & !func<1> & func<0>
  + ALUop<2> & func<3> & !func<2> & func<1> & !func<0>

## Slide 33: Step 5: Logic for each control signal
7.2
nPC_sel <= if (OP == BEQ) then “Br” else “+4”
ALUsrc <= if (OP == “Rtype”) then “regB” else “immed”
ALUctr <= if (OP == “Rtype”) then funct elseif (OP == ORi) then “OR” elseif (OP == BEQ) then “sub” else “add”
ExtOp <= _____________
MemWr <= _____________
MemtoReg <= _____________
RegWr: <=_____________
RegDst: <= _____________

## Slide 34: Step 5: Logic for each control signal
nPC_sel <= if (OP == BEQ) then “Br” else “+4”
ALUsrc <= if (OP == “Rtype”) then “regB” else “immed”
ALUctr <= if (OP == “Rtype”) then funct elseif (OP == ORi) then “OR” elseif (OP == BEQ) then “sub” else “add”
ExtOp <= if (OP == ORi) then “zero” else “sign”
MemWr <= (OP == Store)
MemtoReg <= (OP == Load)
RegWr: <= if ((OP == Store) || (OP == BEQ)) then 0 else 1
RegDst: <= if ((OP == Load) || (OP == ORi)) then 0 else 1

## Slide 35: The “Truth Table” for the Main Control
R-type
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPC_sel
Jump
ExtOp
ALUop (Symbolic)
1
0
0
1
0
0
0
x
“R-type”
0
1
0
1
0
0
0
0
Or
0
1
1
1
0
0
0
1
Add
x
1
x
0
1
0
0
1
Add
x
0
x
0
0
1
0
x
Subtract
x
x
x
0
0
0
1
x
xxx
op
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
ALUop <2>
1
0
0
0
0
x
ALUop <1>
0
1
0
0
0
x
ALUop <0>
0
0
0
0
1
x
Main
Control
op
6
ALU
Control
(Local)
func
3
6
ALUop
ALUctr
3
RegDst
ALUSrc
:

## Slide 36: The “Truth Table” for RegWrite
R-type
ori
lw
sw
beq
jump
RegWrite
1
1
1
0
0
0
op
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
RegWrite = R-type + ori + lw
  = !op<5> & !op<4> & !op<3> & !op<2> & !op<1> & !op<0> (R-type)
  + !op<5> & !op<4> & op<3> & op<2> & !op<1> & op<0> (ori)
  + op<5> & !op<4> & !op<3> & !op<2> & op<1> & op<0> (lw)
op<0>
op<5>
.
.
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
R-type
ori
lw
sw
beq
jump
RegWrite

## Slide 37: PLA Implementation of the Main Control
op<0>
op<5>
.
.
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
R-type
ori
lw
sw
beq
jump
RegWrite
ALUSrc
MemtoReg
MemWrite
Branch
Jump
RegDst
ExtOp
ALUop<2>
ALUop<1>
ALUop<0>

## Slide 38: A Real MIPS Datapath (CNS T0)

## Slide 39: Putting it All Together: A Single Cycle Processor

## Slide 40: Recap: An Abstract View of the Critical Path (Load)
Register file and ideal memory:
  The CLK input is a factor ONLY during write operation
  During read operation, behave as combinational logic:
    Address valid => Output valid after “access time.”
Critical Path (Load Operation) =
PC’s Clk-to-Q +
Instruction Memory’s Access Time +
Register File’s Access Time +
ALU to Perform a 32-bit Add +
Data Memory Access Time +
Setup Time for Register File Write +
Clock Skew
Clk
5
Rw
Ra
Rb
32 32-bit
Registers
Rd
ALU
Clk
Data In
Data
Address
Ideal
Data
Memory
Instruction
Instruction
Address
Ideal
Instruction
Memory
Clk
PC
5
Rs
5
Rt
16
Imm
32
32
32
32
A
B
Next Address

## Slide 41: Worst Case Timing (Load)
Clk
PC
Rs, Rt, Rd,
Op, Func
Clk-to-Q
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA
Register File Access Time
Old Value
New Value
busB
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
ExtOp
Old Value
New Value
ALUSrc
Old Value
New Value
MemtoReg
Old Value
New Value
Address
Old Value
New Value
busW
Old Value
New
Delay through Extender & Mux
Register
Write Occurs
Data Memory Access Time

## Slide 42: Drawback of this Single Cycle Processor
Long cycle time:
  Cycle time must be long enough for the load instruction:
    PC’s Clock -to-Q +
    Instruction Memory Access Time +
    Register File Access Time +
    ALU Delay (address calculation) +
    Data Memory Access Time +
    Register File Setup Time +
    Clock Skew
Cycle time for load is much longer than needed for all other instructions

## Slide 43: Preview
Next Time: MultiCycle Data Path
  CPI  1, CycleTime much shorter (~1/5 of time)

## Slide 44: Summary
Single cycle datapath => CPI=1, CCT => long
5 steps to design a processor
  1. Analyze instruction set => datapath requirements
  2. Select set of datapath components & establish clock methodology
  3. Assemble datapath meeting the requirements
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
  5. Assemble the control logic
Control is the hard part
MIPS makes control easier
  Instructions same size
  Source registers always in same place
  Immediates same size, location
  Operations always on registers/immediates
Control
Datapath
Memory
Processor
Input
Output