## Slide 1: Lecture13 Pipeline II
Computer Organization and Architecture

## Slide 2: Today’s Topic
00
01. Recap
02. Introduction of pipeline
03. Hazard
04. Design a pipeline processor
05. Summary

## Slide 3: Recap: Summary of Pipelining Basics
1
5 stages:
  Fetch: Fetch instruction from memory
  Decode: get register values and decode control information
  Execute: Execute arithmetic operations/calculate addresses
  Memory: Do memory ops (load or store)
  Writeback: Write results back to registers (I.e. COMMIT)
Pipelines pass control information down the pipe just as data moves down pipe
Forwarding/Stalls handled by local control
Balancing length of instructions makes pipelining much smoother
Increasing length of pipe increases impact of hazards; pipelining helps instruction bandwidth, not latency

## Slide 4: Recap: Can pipelining get us into trouble?
1.1
Yes: Pipeline Hazards
  structural hazards: attempt to use the same resource two different ways at the same time
    E.g., combined washer/dryer would be a structural hazard or folder busy doing something else (watching TV)
  data hazards: attempt to use item before it is ready
    E.g., one sock of pair in dryer and one in washer; can’t fold until get sock from washer through dryer
    instruction depends on result of prior instruction still in the pipeline
  control hazards: attempt to make a decision before condition is evaulated
    E.g., washing football uniforms and need to get proper detergent level; need to see after dryer before next load in
    branch instructions
Can always resolve hazards by waiting
  pipeline control must detect the hazard
  take action (or delay action) to resolve hazards

## Slide 5: Pipelining the Load Instruction
1.2
The five independent functional units in the pipeline datapath are:
  Instruction Memory for the Ifetch stage
  Register File’s Read ports (bus A and busB) for the Reg/Dec stage
  ALU for the Exec stage
  Data Memory for the Mem stage
  Register File’s Write port (bus W) for the Wr stage

## Slide 6: The Four Stages of R-type
Ifetch: Instruction Fetch
  Fetch the instruction from the Instruction Memory
Reg/Dec: Registers Fetch and Instruction Decode
Exec:
  ALU operates on the two register operands
  Update PC
Wr: Write the ALU output back to the register file

## Slide 7: Pipelining the R-type and Load Instruction
2.1
We have a structural hazard:
  Two instructions try to write to the register file at the same time!
  Only one write port

## Slide 8: Important Observation
2.2
Each functional unit can only be used once per instruction
Each functional unit must be used at the same stage for all instructions:
  Load uses Register File’s Write Port during its 5th stage
  R-type uses Register File’s Write Port during its 4th stage
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
1
2
3
4
5
Ifetch
Reg/Dec
Exec
Wr
R-type
1
2
3
4
2 ways to solve this pipeline hazard.

## Slide 9: Solution 1: Insert “Bubble”
2.3
Insert a “bubble” into the pipeline to prevent 2 writes at the same cycle
  The control logic can be complex.
  Lose instruction fetch and issue opportunity.
No instruction is started in Cycle 6!

## Slide 10: Solution 2: Delay R-type’s Write
2.4
Delay R-type’s register write by one cycle:
  Now R-type instructions also use Reg File’s write port at Stage 5
  Mem stage is a NOOP stage: nothing is being done.

## Slide 11: Modified Control & Datapath
2.5
IR <- Mem[PC]; PC <– PC+4;
A <- R[rs]; B<– R[rt]
S <– A + B;
R[rd] <– M;
S <– A + SX;
M <– Mem[S]
R[rd] <– M;
S <– A or ZX;
R[rt] <– M;
S <– A + SX;
Mem[S] <- B
if Cond PC < PC+SX;
M <– S
Exec
Reg.
File
Mem
Access
Data
Mem
A
B
S
Reg
File
Equal
PC
Next PC
IR
Inst. Mem
D
M
M <– S

## Slide 12: The Four Stages of Store
2.6
Ifetch: Instruction Fetch
  Fetch the instruction from the Instruction Memory
Reg/Dec: Registers Fetch and Instruction Decode
Exec: Calculate the memory address
Mem: Write the data into the Data Memory

## Slide 13: The Three Stages of Beq
2.7
Ifetch: Instruction Fetch
  Fetch the instruction from the Instruction Memory
Reg/Dec:
  Registers Fetch and Instruction Decode
Exec:
  compares the two register operand,
  select correct branch target address
  latch into PC

## Slide 14: Control Diagram
2.8
IR <- Mem[PC]; PC < PC+4;
A <- R[rs]; B<– R[rt]
S <– A + B;
R[rd] <– S;
S <– A + SX;
M <– Mem[S]
R[rd] <– M;
S <– A or ZX;
R[rt] <– S;
S <– A + SX;
Mem[S] <- B
If Cond PC < PC+SX;
Exec
Reg.
File
Mem
Access
Data
Mem
A
B
S
Reg
File
Equal
PC
Next PC
IR
Inst. Mem
D
M <– S
M <– S
M

## Slide 15: The Big Picture: Where are We Now?
2.9
The Five Classic Components of a Computer
Control
Datapath
Memory
Processor
Input
Output

## Slide 16: Recall: Single cycle control
2.10
Data
Out
Clk
5
Rw
Ra
Rb
32 32-bit
Registers
Rd
ALU
Clk
Data In
Data
Address
Ideal
Data
Memory
Instruction
Instruction
Address
Ideal
Instruction
Memory
Clk
PC
5
Rs
5
Rt
32
32
32
32
A
B
Next Address
Control
Datapath
Control Signals
Conditions

## Slide 17: Data Stationary Control
2.11
The Main Control generates the control signals during Reg/Dec
  Control signals for Exec (ExtOp, ALUSrc, ...) are used 1 cycle later
  Control signals for Mem (MemWr Branch) are used 2 cycles later
  Control signals for Wr (MemtoReg MemWr) are used 3 cycles later
IF/ID Register
ID/Ex Register
Ex/Mem Register
Mem/Wr Register
Reg/Dec
Exec
Mem
ExtOp
ALUOp
RegDst
ALUSrc
Branch
MemWr
MemtoReg
RegWr
Main
Control
ExtOp
ALUOp
RegDst
ALUSrc
MemtoReg
RegWr
MemtoReg
RegWr
MemtoReg
RegWr
Branch
MemWr
Branch
MemWr
Wr

## Slide 18: Datapath + Data Stationary Control
2.12
Exec
Reg.
File
Mem
Access
Data
Mem
A
B
S
Reg
File
PC
Next PC
IR
Inst. Mem
D
Decode
Mem
Ctrl
WB
Ctrl
M
rs
rt
op
rs
rt
fun
im
ex
me
wb
rw
v
me
wb
rw
v
wb
rw
v

## Slide 19: Let’s Try it Out
2.13
10 lw r1, r2(35)
14 addi r2, r2, 3
20 sub r3, r4, r5
24 beq r6, r7, 100
30 ori r8, r9, 17
34 add r10, r11, r12
100 and r13, r14, 15
these addresses are octal

## Slide 20: Start: Fetch 10
00

## Slide 21: Fetch 14, Decode 10

## Slide 22: Fetch 20, Decode 14, Exec 10
3.2

## Slide 23: Fetch 24, Decode 20, Exec 14, Mem 10
3.3

## Slide 24: Fetch 30, Dcd 24, Ex 20, Mem 14, WB 10
3.4

## Slide 25: Fetch 30, Dcd 24, Ex 20, Mem 14, WB 10
3.5

## Slide 26: Fetch 30, Dcd 24, Ex 20, Mem 14, WB 10
3.6

## Slide 27: Fetch 30, Dcd 24, Ex 20, Mem 14, WB 10
3.7

## Slide 28: Fetch 100, Dcd 34, Ex 30, Mem 24, WB 20
3.8

## Slide 29: Fetch 100, Dcd 34, Ex 30, Mem 24, WB 20
3.9

## Slide 30: Fetch 104, Dcd 100, Ex 34, Mem 30, WB 24
3.10

## Slide 31: Fetch 108, Dcd 104, Ex 100, Mem 34, WB 30
3.11

## Slide 32: Fetch 112, Dcd 108, Ex 104, Mem 100, WB 34
3.12

## Slide 33: Pipelined Processor
3.13
Exec
Reg.
File
Mem
Access
Data
Mem
A
B
S
M
Reg
File
Equal
PC
Next PC
IR
Inst. Mem
Valid
IRex
Dcd Ctrl
IRmem
Ex Ctrl
IRwb
Mem Ctrl
WB Ctrl
D
Stalls
Bubbles
Separate control at each stage
Stalls propagate backwards to freeze previous stages
Bubbles in pipeline introduced by placing “Noops” into local stage, stall previous stages.

## Slide 34: Pipeline Hazards Again
3.14
I-Fetch DCD MemOpFetch OpFetch Exec Store
IFetch DCD ° ° °
Structural
Hazard
I-Fet ch DCD OpFetch Jump
IFetch DCD ° ° °
Control Hazard
IF DCD EX Mem WB
IF DCD OF Ex Mem
RAW (read after write) Data Hazard
WAW Data Hazard (write after write)
IF DCD OF Ex RS
WAR Data Hazard (write after read)
IF DCD EX Mem WB
IF DCD EX Mem WB

## Slide 35: Hazard Detection
00
Suppose instruction i is about to be issued and a predecessor instruction j is in the instruction pipeline.
A RAW hazard exists on register if Rregs( i ) Wregs( j )
  Keep a record of pending writes (for inst's in the pipe) and compare with operand regs of current instruction.
  When instruction issues, reserve its result register as a write reservation.
  When on operation completes, remove its write reservation.
A WAW hazard exists on register if Wregs( i ) Wregs( j )
A WAR hazard exists on register if Wregs( i ) Rregs( j )
Window on execution:
Only pending instructions can
cause exceptions
Inst J
Inst I
New Inst
Instruction
Movement:

## Slide 36: Record of Pending Writes In Pipeline Regs
Current operand registers
Pending writes
hazard <=
  ((rs == rwex) & regWex) OR
  ((rs == rwmem) & regWme) OR
  ((rs == rwwb) & regWwb) OR
  ((rt == rwex) & regWex) OR
  ((rt == rwmem) & regWme) OR
  ((rt == rwwb) & regWwb)

## Slide 37: Resolve RAW by “forwarding”
4.1
Detect nearest valid write op operand register and forward into op latches, bypassing remainder of the pipe
Increase muxes to add paths from pipeline registers
Data Forwarding = Data Bypassing

## Slide 38: What about memory operations?
4.2
If instructions are initiated in order and operations always occur in the same stage, there can be no hazards between memory operations!
What about data dependence on loads? R1 <- R4 + R5 R2 <- Mem[ R2 + I ] R3 <- R2 + R1  “Delayed Loads”
Can recognize this in decode stage and introduce bubble while stalling fetch stage
Tricky situation: R1 <- Mem[ R2 + I ] Mem[R3+34] <- R1 Handle with bypass in memory stage!

## Slide 39: Compiler Avoiding Load Stalls:
4.3

## Slide 40: What about Interrupts, Traps, Faults?
4.4
External Interrupts:
  Allow pipeline to drain, Fill with NOPs
  Load PC with interrupt address
Faults (within instruction, restartable)
  Force trap instruction into IF
  disable writes till trap hits WB
  must save multiple PCs or PC + state
Recall: Precise Exceptions  State of the machine is preserved as if program executed up to the offending instruction
  All previous instructions completed
  Offending instruction and all following instructions act as if they have not even started
  Same system code will work on different implementations

## Slide 41: Exception/Interrupts: Implementation questions
4.5
5 instructions, executing in 5 different pipeline stages!
Who caused the interrupt?
  Stage Problem interrupts occurring
  IF Page fault on instruction fetch; misaligned memory access; memory-protection violation
  ID Undefined or illegal opcode
  EX Arithmetic exception
  MEM Page fault on data fetch; misaligned memory access; memory-protection violation; memory error
How do we stop the pipeline? How do we restart it?
Do we interrupt immediately or wait?
How do we sort all of this out to maintain preciseness?

## Slide 42: Exception Handling
4.6
detect bad instruction address
detect bad instruction
detect overflow
detect bad data address
Allow exception to take effect

## Slide 43: Another look at the exception problem
4.7
Use pipeline to sort this out!
  Pass exception status along with instruction.
  Keep track of PCs for every instruction in pipeline.
  Don’t act on exception until it reaches WB stage
Handle interrupts through “faulting no-op” in IF stage
When instruction reaches end of MEM stage:
  Save PC  EPC, Interrupt vector addr  PC
  Turn all instructions in earlier stages into no-ops!
Program Flow
Time
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
Data TLB
Bad Inst
Inst TLB fault
Overflow

## Slide 44: Resolution: Freeze above & Bubble Below
4.8
Flush accomplished by setting “invalid” bit in pipeline
npc
I mem
Regs
B
alu
S
D mem
m
IAU
PC
Regs
A
im
op
rw
n
op
rw
n
op
rw
n
op rw rs rt
bubble
freeze

## Slide 45: Summary
5
Hazards limit performance
  Structural: need more HW resources
  Data: need forwarding, compiler scheduling
  Control: early evaluation & PC, delayed branch, prediction
Data hazards must be handled carefully:
  RAW data hazards handled by forwarding
  WAW and WAR hazards don’t exist in 5-stage pipeline
MIPS I instruction set architecture made pipeline visible (delayed branch, delayed load)
Exceptions in 5-stage pipeline recorded when they occur, but acted on only at WB (end of MEM) stage
  Must flush all previous instructions
More performance from deeper pipelines, parallelism