## Slide 1: Lecture 16 pipeline static schedule
Computer Organization and Architecture

## Slide 2: Review: Pipelining
Key to pipelining: smooth flow
  Making all instructions the same length can increase performance!
Hazards limit performance
  Structural: need more HW resources
  Data: need forwarding, compiler scheduling
  Control: early evaluation & PC, delayed branch, prediction
Data hazards must be handled carefully:
  RAW (Read-After-Write) data hazards handled by forwarding
  WAW (Write-After-Write) and WAR (Write-After-Read) hazards don’t exist in 5-stage pipeline
MIPS I instruction set architecture made pipeline visible (delayed branch, delayed load)
  Change in programmer semantics to make hardware simpler

## Slide 3: Recap: Data Hazards
I-Fet ch DCD MemOpFetch OpFetch Exec Store
IFetch DCD ° ° °
Structural
Hazard
I-Fet ch DCD OpFetch Jump
IFetch DCD ° ° °
Control Hazard
IF DCD EX Mem WB
IF DCD OF Ex Mem
RAW (read after write) Data Hazard
WAW Data Hazard (write after write)
IF DCD OF Ex RS
WAR Data Hazard (write after read)
IF DCD EX Mem WB
IF DCD EX Mem WB

## Slide 4: Recap: Data Stationary Control
The Main Control generates the control signals during Reg/Dec
  Control signals for Exec (ExtOp, ALUSrc, ...) are used 1 cycle later
  Control signals for Mem (MemWr Branch) are used 2 cycles later
  Control signals for Wr (MemtoReg MemWr) are used 3 cycles later
IF/ID Register
ID/Ex Register
Ex/Mem Register
Mem/Wr Register
Reg/Dec
Exec
Mem
ExtOp
ALUOp
RegDst
ALUSrc
Branch
MemWr
MemtoReg
RegWr
Main
Control
ExtOp
ALUOp
RegDst
ALUSrc
MemtoReg
RegWr
MemtoReg
RegWr
MemtoReg
RegWr
Branch
MemWr
Branch
MemWr
Wr
Notes: The main control here is identical to the one in the single cycle processor. It generate all the control signals necessary for a given instruction during that instruction’s Reg/Decode stage.
All these control signals will be saved in the ID/Exec pipeline register at the end of the Reg/Decode cycle.
The control signals for the Exec stage (ALUSrc, ... etc.) come from the output of the ID/Exec register. That is they are delayed ONE cycle from the cycle they are generated.
The rest of the control signals that are not used during the Exec stage is passed down the pipeline and saved in the Exec/Mem register.
The control signals for the Mem stage (MemWr, Branch) come from the output of the Exec/Mem register. That is they are delayed two cycles from the cycle they are generated.
Finally, the control signals for the Wr stage (MemtoReg & RegWr) come from the output of the Exec/Wr register: they are delayed three cycles from the cycle they are generated.
+2 = 45 min. (Y:45)

## Slide 5: Review: Resolve RAW by “forwarding” (or bypassing)
Detect nearest valid write op operand register and forward into op latches, bypassing remainder of the pipe
Increase muxes to add paths from pipeline registers
Data Forwarding = Data Bypassing
npc
I mem
Regs
B
alu
S
D mem
m
IAU
PC
Regs
A
im
op
rw
n
op
rw
n
op
rw
n
op rw rs rt
Forward
mux

## Slide 6: Question: Critical Path???
Bypass path is invariably trouble
Options?
  Make logic really fast
  Move forwarding after muxes
    Problem: screws up branches that require forwarding!
    Use same tricks as “carry-skip” adder to fix this?
    This option may just push delay around….!
  Insert an extra cycle for branches that need forwarding?
    Or: hit common case of forwarding from EX stage and stall for forward from memory?
Regs
B
alu
S
D mem
m
Regs
A
im
Forward
mux
Equal
PC Sel

## Slide 7: Can we somehow make CPI closer to 1?
Let’s assume full pipelining:
  If we have a 4-cycle instruction, then we need 3 instructions between a producing instruction and its use: multf $F0,$F2,$F4 delay-1 delay-2 delay-3 addf $F6,$F10,$F0
Fetch
Decode
Ex1
Ex2
Ex3
Ex4
WB
multf
delay1
delay2
delay3
addf
Earliest forwarding for
4-cycle instructions
Earliest forwarding for
1-cycle instructions

## Slide 8: FP Loop: Where are the Hazards?
Loop: LD F0,0(R1) ;F0=vector element
ADDD F4,F0,F2 ;add scalar from F2
SD 0(R1),F4 ;store result
SUBI R1,R1,8 ;decrement pointer 8B (DW)
BNEZ R1,Loop ;branch R1!=zero
NOP ;delayed branch slot
Instruction Instruction Latency in producing result using result clock cycles
FP ALU op Another FP ALU op 3
FP ALU op Store double 2
Load double FP ALU op 1
Load double Store double 0
Integer op Integer op 0
Where are the stalls?

## Slide 9: FP Loop Showing Stalls
9 clocks: Rewrite code to minimize stalls?
Instruction Instruction Latency in producing result using result clock cycles
FP ALU op Another FP ALU op 3
FP ALU op Store double 2
Load double FP ALU op 1
1 Loop: LD F0,0(R1) ;F0=vector element
2 stall
3 ADDD F4,F0,F2 ;add scalar in F2
4 stall
5 stall
6 SD 0(R1),F4 ;store result
7 SUBI R1,R1,8 ;decrement pointer 8B (DW)
8 BNEZ R1,Loop ;branch R1!=zero
9 stall ;delayed branch slot

## Slide 10: Revised FP Loop Minimizing Stalls
Instruction Instruction Latency in producing result using result clock cycles
FP ALU op Another FP ALU op 3
FP ALU op Store double 2
Load double FP ALU op 1
1 Loop: LD F0,0(R1)
2 stall
3 ADDD F4,F0,F2
4 SUBI R1,R1,8
5 BNEZ R1,Loop ;delayed branch
6 SD 8(R1),F4 ;altered when move past SUBI
Swap BNEZ and SD by changing address of SD
Notes: 3 clocks doing work, 3 overhead (stall, branch, sub)

## Slide 11: Revised FP Loop Minimizing Stalls
Instruction Instruction Latency in producing result using result clock cycles
FP ALU op Another FP ALU op 3
FP ALU op Store double 2
Load double FP ALU op 1
1 Loop: LD F0,0(R1)
2 SUBI R1,R1,8
3 ADDD F4,F0,F2 4
4 BNEZ R1,Loop ;delayed branch
5 SD 8(R1),F4 ;altered when move past SUBI
Swap BNEZ and SD by changing address of SD
Notes: 3 clocks doing work, 3 overhead (stall, branch, sub)

## Slide 12: Unroll Loop Four Times (straightforward way)
1 Loop: LD F0,0(R1)
2 ADDD F4,F0,F2
3 SD 0(R1),F4 ;drop SUBI & BNEZ
4 LD F6,-8(R1)
5 ADDD F8,F6,F2
6 SD -8(R1),F8 ;drop SUBI & BNEZ
7 LD F10,-16(R1)
8 ADDD F12,F10,F2
9 SD -16(R1),F12 ;drop SUBI & BNEZ
10 LD F14,-24(R1)
11 ADDD F16,F14,F2
12 SD -24(R1),F16
13 SUBI R1,R1,#32 ;alter to 4*8
14 BNEZ R1,LOOP
15 NOP
15 + 4 x (1+2) = 27 clock cycles, or 6.8 per iteration
Assumes R1 is multiple of 4
Rewrite loop to minimize stalls?
1 cycle stall
2 cycles stall

## Slide 13: Unrolled Loop That Minimizes Stalls
What assumptions made when moved code?
  OK to move store past SUBI even though changes register
  OK to move loads before stores: get right data?
  When is it safe for compiler to do such changes?
1 Loop: LD F0,0(R1)
2 LD F6,-8(R1)
3 LD F10,-16(R1)
4 LD F14,-24(R1)
5 ADDD F4,F0,F2
6 ADDD F8,F6,F2
7 ADDD F12,F10,F2
8 ADDD F16,F14,F2
9 SD 0(R1),F4
10 SD -8(R1),F8
11 SD -16(R1),F12
12 SUBI R1,R1,#32
13 BNEZ R1,LOOP
14 SD 8(R1),F16 ; 8-32 = -24
14 clock cycles, or 3.5 per iteration
When safe to move instructions?

## Slide 14: Getting CPI < 1: Issuing Multiple Instructions/Cycle
Two main variations: Superscalar and VLIW
Superscalar: varying no. instructions/cycle (1 to 6)
  Parallelism and dependencies determined/resolved by HW
  IBM PowerPC 604, Sun UltraSparc, DEC Alpha 21164, HP 7100
Very Long Instruction Words (VLIW): fixed number of instructions (16) parallelism determined by compiler
  Pipeline is exposed; compiler must schedule delays to get right result
Explicit Parallel Instruction Computer (EPIC)/ Intel
  128 bit packets containing 3 instructions (can execute sequentially)
  Can link 128 bit packets together to allow more parallelism
  Compiler determines parallelism, HW checks dependencies and fowards/stalls

## Slide 15: Getting CPI < 1: Issuing Multiple Instructions/Cycle
Superscalar DLX: 2 instructions, 1 FP & 1 anything else
  – Fetch 64-bits/clock cycle; Int on left, FP on right
  – Can only issue 2nd instruction if 1st instruction issues
  – More ports for FP registers to do FP load & FP op in a pair
Type Pipe Stages
Int. instruction IF ID EX MEM WB
FP instruction IF ID EX MEM WB
Int. instruction IF ID EX MEM WB
FP instruction IF ID EX MEM WB
Int. instruction IF ID EX MEM WB
FP instruction IF ID EX MEM WB
1 cycle load delay expands to 3 instructions in SS
  instruction in right half can’t use it, nor instructions in next slot

## Slide 16: Loop Unrolling in Superscalar
Integer instruction FP instruction Clock cycle
Loop: LD F0,0(R1) 1
LD F6,-8(R1) 2
LD F10,-16(R1) ADDD F4,F0,F2 3
LD F14,-24(R1) ADDD F8,F6,F2 4
LD F18,-32(R1) ADDD F12,F10,F2 5
SD 0(R1),F4 ADDD F16,F14,F2 6
SD -8(R1),F8 ADDD F20,F18,F2 7
SD -16(R1),F12 8
SD -24(R1),F16 9
SUBI R1,R1,#40 10
BNEZ R1,LOOP 11
SD -32(R1),F20 12
Unrolled 5 times to avoid delays (+1 due to SS)
12 clocks, or 2.4 clocks per iteration

## Slide 17: Limits of Superscalar
While Integer/FP split is simple for the HW, get CPI of 0.5 only for programs with:
  Exactly 50% FP operations
  No hazards
If more instructions issue at same time, greater difficulty of decode and issue
  Even 2-scalar => examine 2 opcodes, 6 register specifiers, & decide if 1 or 2 instructions can issue
VLIW: tradeoff instruction space for simple decoding
  The long instruction word has room for many operations
  By definition, all the operations the compiler puts in the long instruction word can execute in parallel
  E.g., 2 integer operations, 2 FP ops, 2 Memory refs, 1 branch
    16 to 24 bits per field => 7*16 or 112 bits to 7*24 or 168 bits wide
  Need compiling technique that schedules across several branches

## Slide 18: Loop Unrolling in VLIW
Memory Memory FP FP Int. op/ Clock reference 1 reference 2 operation 1 op. 2 branch
LD F0,0(R1) LD F6,-8(R1) 1
LD F10,-16(R1) LD F14,-24(R1) 2
LD F18,-32(R1) LD F22,-40(R1) ADDD F4, F0, F2 ADDD F8,F6,F2 3
LD F26,-48(R1) ADDD F12, F10, F2 ADDD F16,F14,F2 4
ADDD F20, F18, F2 ADDD F24,F22,F2 5
SD 0(R1),F4 SD -8(R1),F8 ADDD F28, F26, F2 6
SD -16(R1),F12 SD -24(R1),F16 7
SD -32(R1),F20 SD -40(R1),F24 SUBI R1,R1,#48 8
SD -0(R1),F28 BNEZ R1,LOOP 9
Unrolled 7 times to avoid delays 7 results in 9 clocks, or 1.3 clocks per iteration
Need more registers in VLIW(EPIC => 128int + 128FP)

## Slide 19: Software Pipelining
Observation: if iterations from loops are independent, then can get more ILP by taking instructions from different iterations
Software pipelining: reorganizes loops so that each iteration is made from instructions chosen from different iterations of the original loop (­ Tomasulo in SW)

## Slide 20: Software Pipelining Example
Loop: LD F0,0(R1) ADDD F4,F0,F2 RAW
SD 0(R1),F4 RAW
SUBI R1,R1,8 BNEZ R1,Loop
NOP
LD F0,0(R1) |  | 
ADDD F4,F0,F2 | LD F0,-8(R1) | 
SD 0(R1),F4 | ADDD F4,F0,F2 | LD F0,-16(R1)
 | SD -8(R1),F4 | ADDD F4,F0,F2
 |  | SD -16(R1),F4
Notes: 绿色：装入代码；红色：循环主题；蓝色：排空代码
三道题理解软件流水 - BBMAN - 博客园 (cnblogs.com)

## Slide 21: Software Pipelining Example
LD F0,0(R1) |  | 
ADDD F4,F0,F2 | LD F0,-8(R1) | 
SD 0(R1),F4 | ADDD F4,F0,F2 | LD F0,-16(R1)
 | SD -8(R1),F4 | ADDD F4,F0,F2
 |  | SD -16(R1),F4
LD F0,0(R1)
ADDD F4,F0,F2
LD F0,-8(R1)
SD 0(R1),F4 ADDD F4,F0,F2 LD F0,-16(R1) SD -8(R1),F4 ADDD F4,F0,F2 SD -16(R1),F4

## Slide 22: Software Pipelining Example
LD F0,0(R1)
ADDD F4,F0,F2
LD F0,-8(R1)
SD 0(R1),F4 ADDD F4,F0,F2 LD F0,-16(R1) SD -8(R1),F4 ADDD F4,F0,F2 SD -16(R1),F4
LD F0,0(R1)
ADDD F4,F0,F2
LD F0,0(R1)
SUB R1, R1, 24 LOOP: SD 0(R1),F4 ADDD F4,F0,F2 LD F0,0(R1) BNE R1, LOOP SUB R1, R1, #8 SD 0(R1),F4 ADDD F4,F0,F2 ADDD F4,F0,F2

## Slide 23: Software Pipelining Example
Before: Unrolled 3 times
1 LD F0,0(R1)
2 ADDD F4,F0,F2
3 SD 0(R1),F4
4 LD F6,-8(R1)
5 ADDD F8,F6,F2
6 SD -8(R1),F8
7 LD F10,-16(R1)
8 ADDD F12,F10,F2
9 SD -16(R1),F12
10 SUBI R1,R1,#24
11 BNEZ R1,LOOP
After: Software Pipelined
1 SD 0(R1),F4 ; Stores M[i]
2 ADDD F4,F0,F2 ; Adds to M[i-1]
3 LD F0,-16(R1); Loads M[i-2]
4 SUBI R1,R1,#8
5 BNEZ R1,LOOP
Symbolic Loop Unrolling
Maximize result-use distance
Less code space than unrolling
Fill & drain pipe only once per loop vs. once per each unrolled iteration in loop unrolling
SW Pipeline
Loop Unrolled
overlapped ops
Time
Time
Notes: 绿色：装入代码；红色：循环主题；蓝色：排空代码

## Slide 24: Software Pipelining with Loop Unrolling in VLIW
Memory Memory FP FP Int. op/ Clock
reference 1 reference 2 operation 1 op. 2 branch
LD F0,-48(R1) ST 0(R1),F4 ADDD F4,F0,F2 1
LD F6,-56(R1) ST -8(R1),F8 ADDD F8,F6,F2 SUBI R1,R1,#24 2
LD F10,-40(R1) ST 8(R1),F12 ADDD F12,F10,F2 BNEZ R1,LOOP 3
Software pipelined across 9 iterations of original loop
  In each iteration of above loop, we:
    Store to m,m-8,m-16 (iterations I-3,I-2,I-1)
    Compute for m-24,m-32,m-40 (iterations I,I+1,I+2)
    Load from m-48,m-56,m-64 (iterations I+3,I+4,I+5)
9 results in 9 cycles, or 1 clock per iteration
Average: 3.3 ops per clock, 66% efficiency
Note: Need less registers for software pipelining
(only using 7 registers here, was using 15)

## Slide 25: Can we use HW to get CPI closer to 1?
Why in HW at run time?
  Works when can’t know real dependence at compile time
  Compiler simpler
  Code for one machine runs well on another
Key idea: Allow instructions behind stall to proceed: DIVD F0,F2,F4 ADDD F10,F0,F8 SUBD F12,F8,F14
Out-of-order execution => out-of-order completion.
Disadvantages?
  Complexity
  Precise interrupts harder! (Talk about this next time)

## Slide 26: Problems?
How do we prevent WAR and WAW hazards?
How do we deal with variable latency?
  Forwarding for RAW hazards harder.
RAW
WAR

## Slide 27: Summary
Precise interrupts are easy to implement in a 5-stage pipeline:
  Mark exception on pipeline state rather than acting on it
  Handle exceptions at one place in pipeline (memory-stage/beginning of writeback)
Loop unrolling  Multiple iterations of loop in software:
  Amortizes loop overhead over several iterations
  Gives more opportunity for scheduling around stalls
Software Pipelining  take one instruction from each of several iterations of the loop
  Software overlapping of loop iterations
Very Long Instruction Word machines (VLIW)  Multiple operations coded in single, long instruction
  Requires compiler to decide which ops can be done in parallel
  Trace scheduling  find common path and schedule code as if branches didn’t exist (+ add “fixup code”)