## Slide 1
Computer Organization and Architecture
Lecture16 Memory(I)-SRAM & DRAM

## Slide 2: Today’s Topic
00
01. Introduction
02. SRAM
03. DRAM Device
04. Memory Subsystem

## Slide 3: The Big Picture: Where are We Now?
01
The Five Classic Components of a Computer
Today’s Topics:
  SRAM Memory Technology
  DRAM Memory Technology
  Memory Organization
Control
Datapath
Memory
Processor
Input
Output

## Slide 4: Random Access Memory (RAM) Technology
1.2
Why do computer designers need to know about RAM technology?
  Processor performance is usually limited by memory bandwidth
  As IC densities increase, lots of memory will fit on processor chip
    Tailor on-chip memory to specific needs
      Instruction cache
      Data cache
      Write buffer
What makes RAM different from a bunch of flip-flops?
  Density: RAM is much denser

## Slide 5: Today’s Topic
00
01. Introduction
02. SRAM
03. DRAM Device
04. Memory Subsystem

## Slide 6: Static RAM (SRAM) Cell
2.1
6-Transistor SRAM Cell
bit
bit
word
(row select)
bit
bit
word
Write:
  1. Drive bit lines (bit=1, bit=0)
  2. Select row
Read:
  1. Precharge bit and bit to Vdd or Vdd/2 => make sure equal!
  2.. Select row
  3. Cell pulls one line low
  4. Sense amp on column detects difference between bit and bit
replaced with pullup
to save area
1
0
0
1

## Slide 7: Typical SRAM Organization: 16-word x 4-bit
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
-
+
Sense Amp
-
+
Sense Amp
-
+
Sense Amp
-
+
Sense Amp
:
:
:
:
Word 0
Word 1
Word 15
Dout 0
Dout 1
Dout 2
Dout 3
-
+
Wr Driver &
Precharger
-
+
Wr Driver &
Precharger
-
+
Wr Driver &
Precharger
-
+
Wr Driver &
Precharger
Address Decoder
WrEn
Precharge
Din 0
Din 1
Din 2
Din 3
A0
A1
A2
A3
Q: Which is longer:
word line or
bit line?
2.2

## Slide 8: Logic Diagram of a Typical SRAM
2.3
A
D
OE_L
2
N
words
x M bit
SRAM
N
M
WE_L
Write Enable is usually active low (WE_L)
Din and Dout are combined to save pins:
  A new control signal, output enable (OE_L) is needed
  WE_L is asserted (Low), OE_L is disasserted (High)
        D serves as the data input pin
  WE_L is disasserted (High), OE_L is asserted (Low)
    D is the data output pin
  Both WE_L and OE_L are asserted:
    Result is unknown. Don’t do that!!!

## Slide 9: Typical SRAM Timing
2.4
Write Timing:
D
Read Timing:
WE_L
A
Write
Hold Time
Write Setup Time
A
D
OE_L
2
N
words
x M bit
SRAM
N
M
WE_L
Data In
Write Address
OE_L
High Z
Read Address
Junk
Read Access
Time
Data Out
Read Access
Time
Data Out
Read Address

## Slide 10: Analyze the SRAM Cell
2.5
6-Transistor SRAM Cell
bit
bit
word
(row select)
bit
bit
word
1
0
0
1
P1 P2
N1 N2
An SRAM chip usually contains a great amount of word (row)
  Very long bit lines => large capacitors
  P1, P2, N1 and N2 must be very small
N1 and P1 have no enough energy to drive the bit line
  Add a sense amplifier to compare Bit and Bit

## Slide 11: Construct Register File with SRAM cells
2.6
Write new value into a cell:
  drive both sides (two NMOS in red color) simultaneously
  Can only write one word at every write operation
Additional bit line pair(w and w bar)
  read and write can be done simultaneously

## Slide 12: RF with 2 read ports and 1 write port
2.6

## Slide 13: Problems with SRAM
2.7
Six transistors use up a lot of area
Consider a “Zero” is stored in the cell:
  Transistor N1 will try to pull “bit” to 0
  Transistor P2 will try to pull “bit bar” to 1
But bit lines are precharged to high: Are P1 and P2 necessary?
bit = 1
bit = 0
Select = 1
On
Off
Off
On
N1
N2
P1
P2
On
On

## Slide 14: Today’s Topic
00
01. Introduction
02. SRAM
03. DRAM Device
04. Memory Subsystem

## Slide 15: 1-Transistor Memory Cell (DRAM)
3.1
Write:
  1. Drive bit line
  2.. Select row
Read:
  1. Precharge bit line to Vdd/2
  2.. Select row
  3. Cell and bit line share charges
    Very small voltage changes on the bit line
  4. Sense (fancy sense amp)
    Can detect changes of ~1 million electrons
  5. Write: restore the value
Refresh
  1. Just do a dummy read to every cell.
row select
bit

## Slide 16: Classical DRAM Organization (square)
3.2
r
o
w
d
e
c
o
d
e
r
row
address
Column Selector &
I/O Circuits
Column
Address
data
RAM Cell
Array
word (row) select
bit (data) lines
Row and Column Address together:
  Select 1 bit a time
Each intersection represents
a 1-T DRAM Cell

## Slide 17: DRAM Operation: Three Steps
3.3
Precharge
  Charges bit lines to know value, reqired before next row access
Row access(RAS)
  decode row address, enable addressed row (often multiple Kb in row)
  Contents of storage cell share charge with bitlines
  Small change in voltage detected by sense amplifiers (SAs) which latch whole row bits
  sense amplifiers drive bitlines full rail to recharge storage cells
Column access (CAS)
  decode column address to select small number of SA latches (4,8,16 or 32 bits depending on DRAM package
  on read, send latched bits out to chip pins
  on write, change SA latches, which then charge storage cells to reqired value
  can perform multiple column access on same row without another row access (burst mode)

## Slide 18: DRAM access protocol
3.4
5 basic commands
  ACTIVATE
  READ
  WRITE
  PRECHARGE
  REFRESH
To reduce pin count, row and column share same address pins
  RAS=Row Address Strobe
  CAS=Column Address Strobe

## Slide 19: DRAM Bank Operation
3.5
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 0, Column 85)
Column address 85
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:

## Slide 20: DRAM Basic Operation
3.5
Access to an “ open row”
  No need for ACTIVATE command
  READ/WRITE to access row buffer
Access to a “ closed row”
  If another row already active, must first issue PRECHAGE
  ACTIVATE to open new row
  READ/WRITE to access row buffer
  Optional: PRECHARGE after READ/WRITESs finished

## Slide 21: DRAM Timing--READ (Example)
3.6
Every DRAM access begins at:
  The assertion of the RAS_L
  2 ways to read:
    Early or late v. CAS

## Slide 22: DRAM Timing-WRITE (Example)
3.6
Every DRAM access begins at:
  The assertion of the RAS_L
  2 ways to read:
    Early or late v. CAS

## Slide 23: DRAM Timing-Burst
3.6
Each READ/WRITE command can transfer multiple words (8 in DDR3)
Critical word first?

## Slide 24: DRAM: Banks
3.7
Modern DRAM chips consist of multiple banks
  Address=(Bank x, Row y, Column z)
Banks operate independently, but share
command/address/data pins
  Each can have a different row active
  Can overlap ACTIVATE and PRECHARGE latencies!
    (i.e. READ to bank 0 while ACTIVATING bank 1)

## Slide 25: DRAM: Banks
3.7
Enable concurrent DRAM accesses (overlapping)

## Slide 26: Quest for DRAM Performance
3.8
Fast Page mode
  Adding timing signals that allow repeated accesses to row buffer without another row access time
  Such a buffer comes naturally, as each array will buffer 1024 to 2048 bits for each access
Synchronous DRAM (SDRAM)
  Add a clock signal to DRAM interface, so that the repeated transfers would not bear overhead to synchronize with DRAM controller
Double Data Rate (DDR SDRAM)
  Transfer data on both the rising edge and falling edge of the DRAM clock signal => doubling the peak data rate
  DDR2 lowers power by dropping the voltage from 2.5 to 1.8 volts + offers high clock rates: up to 400 MHz
  DDR3 drops to 1.5 volts + high clock rates: up to 800 MHz
  DDR4 drops to 1-1.2 volts + high clock rates: up to 1600 MHz

## Slide 27: Fast Page Mode Operation
3.8.1
Regular DRAM Organization:
  N rows x N column x M-bit
  Read & Write M-bit at a time
  Each M-bit access requires a RAS / CAS cycle
Fast Page Mode DRAM
  N x M “SRAM” to save a row
After a row is read into the register
  Only CAS is needed to access other M-bit blocks on that row
  RAS_L remains asserted while CAS_L is toggled

## Slide 28: SDRAM timing (Single Data Rate)
3.8.2
RAS
(New Bank)
CAS
Burst READ
Precharge
Micron 128M-bit DRAM (Using 2Meg X 16 bit X 4 bank ver)
-Row (12 bits), bank (2 bits), Column (9 bits)

## Slide 29: Double-Data-Rate (DDR2) DRAM
3.8.3
[Micron, 256 Mb DDR2 Datasheet]
400 Mb/S Data Rate
ROW
Column
Precharge
ROW
Data

## Slide 30: Today’s Topic
00
01. Introduction
02. SRAM
03. DRAM Device
04. Memory Subsystem

## Slide 31: Memory subsystem organization
4

## Slide 32: Memory sybsystem
4

## Slide 33: Breaking down a DIMM
4.1
Notes: In computing, serial presence detect (SPD) is a standardized way to automatically access information about a memory module.
Some computers adapt to hardware changes completely automatically. In most cases, there is a special optional procedure for accessing BIOS parameters, to view and potentially make changes in settings. It may be possible to control how the computer uses the memory SPD data—to choose settings, selectively modify memory timings, or possibly to completely over-ride the SPD data. This unit is essential for modern computer memories, especially overclocking computers.

## Slide 34: Breaking down a DIMM
4.1

## Slide 35: Rank
4.2

## Slide 36: Breaking down a Rank
4.2

## Slide 37: Breaking down a Chip
4.3

## Slide 38: Breaking down a Bank
4.4

## Slide 39: Example: Transferring a cache block
4.5

## Slide 40: Example: Transferring a cache block
4.5

## Slide 41: Example: Transferring a cache block
4.5

## Slide 42: Example: Transferring a cache block
4.5

## Slide 43: Example: Transferring a cache block
4.5

## Slide 44: Example: Transferring a cache block
4.5

## Slide 45: Example: Transferring a cache block
4.5

## Slide 46: DRAM Overview (DRAM Modules)
4.6

## Slide 47: DRAM Modules
4.6
DRAM chips have narrow interface (typically X4, X8, X16)
Multiple chips are put together to form a wide interface
  DIMM: Dual Inline Memory Module
  TO get a 64-bit DIMM, we need to access 8 chips with 8-bit interfaces
  Share command/address lines, but not data
Advantages
  Acts like a high-capacity DRAM chip with a wide interface
    8x capacity, 8x bandwidth, same latency
Disadvantages
  Granularity: Accesses cannot be smaller than the interface width
    8x power

## Slide 48: A 64-bit Wide DIMM (physical view)
4.7

## Slide 49: A 64-bit Wide DIMM (physical view)
4.8

## Slide 50: DRAM Ranks
4.9
A DIMM may include multiple Ranks
  A 64-bit DIMM using 8 chips with X16 interfaces has 2 ranks
Each 64-bit group of chips is called a rank
  All chips in a rank respond to a single command
  Different ranks share command/address/data lines
  Select between ranks with “Chip Select” signal
  Ranks provide more “banks” across multiple chips
  (but don’t confuse rank and bank!)

## Slide 51: Multiple DIMM on a Channel
4.10
Advantages
  Enable even higher capacity
Disadvantages
  Interconnect latency, complexity, and energy get higher
  Addr/Cmd signal integrity is a challenge

## Slide 52: DRAM Channels
4.11

## Slide 53: DRAM Channels
4.11
Channel: a set of DIMMs in series
  All DIMMs get the same command, one of the ranks replies
System options
  Single channel system
  Multiple dependent (lock-step) channels
    Single controller with wider interface (faster cache line refill!)
    Sometimes called “Gang Mode”
    Only works if DIMMs are identical (organization, timing)
  Multiple independent channels
    Requires multiple controllers
Tradeoffs
  Cost: pins, wires, controller
  Benefit: higher bandwidth, capacity, flexibility

## Slide 54: DRAM Channel Options
4.11

## Slide 55: Memory Controller
4.12

## Slide 56: DRAM：Timing Constraints
4.12
Memory controller must respect physical device characteristics
  tRCD=Row to Column command delay
    How long it takes row to get to sense amps
  tCAS=Time between column command and data out
  tCCD=Time between column commands
    Rate that you can pipeline column commands
  tRP=Time to precharge DRAM array
  tRAS=Time between RAS and data restoration in DRAM array (minimum time a row must be open)
  tRC=tRAS+tRP=Row “cycle” time
    Minimum time between accesses to different rows

## Slide 57: DRAM: Timing Constraints
4.12
There are dozens of these…
  tWTR=Write to read delay
  tWR =Time from end of last write to PRECHARGE
  tFAW=Four ACTIVATE window (limits current surge)
Makes performance analysis, memory controller design difficult
Datasheets for DRAM devices freely available on website

## Slide 58: Latency Components: Basic Operation
4.12
CPU-> controller transfer time
Controller latency
  Queuing & scheduling delay at the controller
  Access converted to basic commands
DRAM bank latency
  tCAS is row “open” OR
  tRCD +tCAS if array precharge OR
  tRP+tRCD+tCAS (worst case:tRC+tRCD+tCAS)
DRAM data transfer time
  BurstLen/(MT/S) (500MHz DDR=1000 MT/S)
Controller ->CPU transfer time

## Slide 59: DRAM Addressing
4.12

## Slide 60: DRAM Controller Functionality
4.12
Translate memory requests into DRAM command sequences
  Map “physical Address” to DRAM Address
  Obey timing constraints of DRAM, arbitrate resource confilicts (i.e. bank, channel)
Buffer and schedule requests to improve performance
  Row-buffer management and re-ordering
Ensure correct operation of DRAM (refresh)
Manage power consumption and thermals in DRAM
  Turn on/off DRAM chips, manage power modes

## Slide 61: A Modern DRAM Controller
4.12

## Slide 62: Row Buffer Management Policies
4.12
Open row
  Keep the open after an access
  Pro: Next access might need the same row -> row hit
  Con:Next access might need a different row -> row conflict, wasted energy
Closed row
  Close the row after an access ( if no other requests already in the request buffer need the same row)
  Pro: Next access might need a different row -> avoid a row conflict
  Con: Next access might need the same row -> extra activate latency
Adaptive policies
  Predict whether or nor the next access to the bank will be to the same row

## Slide 63: DRAM Controller Scheduling Policies(I)
4.12
FCFS (first come first served)
  Oldest request first
FR-FCFS (first ready, first come first served)
  Row-hit first
  Oldest first
  Goal:Maximize row buffer hit rate-> Maximize DRAM throughput

## Slide 64: DRAM Controller Scheduling Policies (II)
4.12
A Scheduling Policy is a prioritization order
Prioritization can be based on
  Request age
  Row buffer hit/miss status
  Request type (prefetch, read, write)
  Requestor type (load miss or store miss)
  Request criticality
    Oldest miss in the core?
    How many instructions in core are dependent on it?

## Slide 65: DRAM Refresh (I)
4.12
DRAM capacitor charge leaks over time
The memory controller needs to read each row periodically to restore the charge
  Activate + precharge each row every N ms
  Typical N=64ms
Implications on Performance?
  DRAM bank unavailable while refreshed
  Long pause times: If we refresh all rows in burst, every 64ms the DRAM will be unavailable until refresh ends.

## Slide 66: DRAM Refresh (II)
4.12
Distributed refresh eliminates long pause times
How else can we reduce the effect of refresh on performance?
  Can we reduce the number of refreshes?

## Slide 67: DRAM Controllers are difficult to Design
4.12
Need to obey DRAM timing constraints for correctness
  There are many (50+) timing constraints in DRAM
Need to keep track of many resources to prevent conflicts
  Channels, banks, ranks, data bus, address bus, row buffers
Need to handle DRAM refresh
Need to optimize for performance (in the presence of constraints)
  Reordering is not simple
  Predicting the future?

## Slide 68: DRAM Power Management
4.13
DRAM chips have power modes
Idea: When not accessing a chip power it down
Power states
  Active (highest power)
  All banks idle (i.e. precharged)
  Power-down
  Self-refresh (lowest power)
State transitions incur latency during which the chip cannot be accessed

## Slide 69: Technology Trends (from 1st lecture)
1.1

## Slide 70: Technology Trends (from 1st lecture)
1.1

## Slide 71: Who Cares About the Memory Hierarchy?
1.2